CRYOVEX 2008

Final Report

S. M. Hvidegaard, R. Forsberg V. Helm, H. Skourup, and L. Stenseng

DTU Space, March 2009, Draft 1

Table of Contents

Introduction	3

1	Summary of operations	4

2	Hardware Installation	7

3	Acquired data	10

4	Processing	11

4.1	GPS data processing	11

4.2	INS and GPS data merging	12

4.3	Laser scanner data processing	13

4.4	ASIRAS radar data processing	20

4.5	Auxilary data	21

5	Validation Sites	23

5.1	Northern Greenland Ice Sheet - UK1	23

5.2	Alert Sea Ice	24

5.3	Devon Ice Cap	26

5.4	Others: Ilulissat and Fram Strait	27

6	Conclusions	30

7	References	31

8	Appendix	32

8.1	Operator logs	32

8.2	File formats	50

8.3	GPS reference coordinates	53

8.4	Corner reflector details from sea ice in-situ observations	53

8.5	ASIRAS data files	54

8.6	Processed ASIRAS profiles	62

Introduction

The European Space Agency (ESA) CryoSat Validation Experiment, CryoVEx 2008 was carried out in April and May 2008. The airborne operations were coordinated by the National Space Institute, Danish Technical University (DTU Space) and took place in the period April 15 to May 8. The work consisted of:

- Airborne data collection with ASIRAS and laser scanner system. The operations were coordinated with ground and helicopter activities over land and sea ice in Greenland and Canada.

- Logistical support for participants in the CryoVEx 2008 experiment especially concerning transport and access to military facilities in Canadian Forces Station Alert and Thule Air Base as well as aircraft support to the UK team on the north Greenland ice sheet.

Figure 1 shows the full flight tracks for the airborne Twin Otter operation in April and May 2008.

Figure 1. Flight tracks for airborne Twin Otter observations

This report outlines the airborne field operations and the processing of the data acquired during the CryoVEx 2008 campaign. In addition examples from the processed datasets will be presented.

# Summary of operations

The DTU Space operations started out on April 15 in Kangerlussuaq, Greenland, with installation of the laser scanner and ASIRAS system in the Air Greenland Twin Otter reg. OY-POF following the same procedures as certified in 2006. Due to a minor technical problem with the Twin Otter the aircraft was not available until the 16th. This did not affect the installation since the first day was spent on retrieving the cargo with the equipment and unpacking the boxes. Assistance with the ASIRAS system was provided by Raumfahrt Systemtechnik’s engineer.

After installing the equipment in the Air Greenland hanger and performing ground tests, a successful test flight was carried out on April 17th. Apart from minor problems with the backup system for the laser measurements – INS and laser altimeter – the full system of laser scanner and ASIRAS was working as expected. The problems with the backup system were sorted out on ground prior to the next flights.

The next two days were spent on a survey for the Bureau of Minerals and Petroleum, BMP, Greenland  Homerule Government, monitoring the sea ice off the Greenland west coast near Upernavik. After this the EGIG line was surveyed April 20th on transit from Ilulissat to Constable Pynt on the east coast. En route, observations on a line near Ilulissat, both High Altitude and Low Altitude ASIRAS data were gathered.

Next the Twin Otter continued to St. Nord, northeast Greenland, where again observation was carried out for the BMP. On April 26th a coordinated flight was carried out near KV Svalbard, the coast guard vessel from Svalbard, which was on a scientific cruise in the Fram Strait. The ship was anchored to an ice floe that was surveyed with the airborne system as well as on the surface from the ship in coordination with the Norwegian Polar Institute. From St. Nord a second survey was done on April 27th in order to re-measure lines north of Greenland.

On April 28th the aircraft continued to CFS Alert to meet the ground teams there, who flew in from Canada and Qaanaaq, North Greenland, with dedicated Twin Otter flights (chartered from Ken Borek) on April 28th and 30th.

In the meantime the other Air Greenland Twin Otter reg. OY-ATY equipped with skies deployed the UK1 team, of Liz Morris and Martin Hignell, on the ice sheet in northern Greenland via Qaanaaq and Thule Air Base. These operations were delayed by poor weather and took place from April 23rd to 25th and consisted of transport from Kangerlussuaq to Qaanaaq on April 23rd and put in on the ice over the next two days including deployment of two depots with fuel and other supplies for the transect.

From Alert lines were surveyed in the Arctic Ocean on May 1st and 2nd. In addition the validation sites near the coast were observed on May 1st and on May 2nd a coordinated line was flown with the helicopter-borne EM bird system from Alfred Wegener Institute/University of Alberta, Edmonton.

A second coordinated helicopter and Twin Otter flight was cancelled in the last minute on May 5th due to poor visibility. The Twin Otter flew a few survey lines near the AUV (Autonomous Underwater Vehicle) camp just off the coast but this also had to be altered to a lower altitude due to low clouds. Afterwards, the aircraft-team continued to Thule Air Base via Grant Ice Cap and Mt. Oxford on Ellesmere Island to position the Twin Otter for operations over Devon Island. Initially it was planned to use the small inuit settlement Grise Fiord as base for the Devon survey but the weather favoured operations out of the larger and better equipped airfield in Thule.

The Devon ice cap was then surveyed on May 6th where the main lines N-S and E-W was flown repeatedly to ensure corner reflector hits and a few lines suggested by the Canadian team was also surveyed.

After the Devon flight the Twin Otter returned to Kangerlussuaq on May 7th to be used for a test campaign for the DTU Space P-Sounder instrument. The ASIRAS system was un-mounted and returned to RST.

Table 1 gives an overview of the specific flights in chronological order and below a short day-to-day description is found.

Day2day

April 15-17	Installation and test of ASIRAS and laser scanner system on Twin Otter

April 18	Survey of icebergs near Ilulissat for DMI and local flight for Danish Television reporters

April 19	Sea ice observations coordinated with helicopter in-situ measurements off the west coast near Upernavik

April 20	Transit to the east coast with survey of CryoSat line near Ilulissat and the EGIG line across the ice sheet

April 21	Transit to St. Nord after cancellation of helicopter operations near the east coast due to ice fog in survey area. Some observations with laser and ASIRAS en route with refuelling in Daneborg

April 22-23	No flights due to bad weather in St. Nord

April 24	Over-flight of KV Svalbard in the Fram Strait and survey of E-W lines between St. Nord and Danmarkshavn. Refueling in Danmarkshavn

April 25-26	No flights due to bad weather in St. Nord

April 27	Observation on lines north of Greenland

April 28	Transit to Alert with survey of sea ice near the coast and parts of the coast of northern Greenland

April 29	Survey of the UK1 site on the northern ice sheet

April 30	Dense fog at Alert – no flights

May 1	Survey of long lines north-east and survey of validation sites near Alert in the afternoon

May 2	Survey of square north-west and coordinated flight of N-S line in the afternoon

May 3	Snow and dense fog – no flights

May 4	Planned afternoon flight with helicopter but had to cancel due to bad weather

May 5	Planned coordinated helicopter flight cancelled due to low clouds. Survey of AUV site altered to low altitude followed by survey of Grant Ice Cap, Ellesmere Island, en route to Thule

May 6	Devon ice cap survey

May 7	Return to Kangerlussuaq with sea ice observations en route and survey over Disko Island

May 8-	Un-mount ASIRAS and P-sounder test

The airborne field team consisted of:

DTU Space: Sine M. Hvidegaard (SMH), Lars Stenseng (LS), and Henriette Skourup (HSK).

RST: Harald Lentz (HL).

Table 1. Flight details

| Date/JD | Flight | Track | Off block UTC | Take off UTC | Landing UTC | On block UTC | Air-borne | Survey operators |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 108/Apr 17 | Test/drop | SFJ-SFJ | 1837 | 1842 | 1955 | 2000 | 1h18 | SMH/LS/HL |
| 109/Apr 18 | ICB | JAV-SFJ | 1448 | 1453 | 1616 | 1621 | 1h33 | SMH/LS |
| 109/Apr 18 | Journalists | JAV-JAV | 1756 | 1801 | 1835 | 1840 | 0h44 | SMH/LS |
| 110/Apr 19 | K1-K4 | JAV-JUV | 1023 | 1028 | 1443 | 1448 | 4h25 | SMH/LS |
| 110/Apr 19 | K5-HE-K8 | JUV-JAV | 1552 | 1557 | 2108 | 2113 | 5h21 | SMH/LS |
| 111/Apr 20 | JAV-T-EG | JAV-CNP | 1119 | 1124 | 1548 | 1553 | 4h34 | SMH/LS |
| 112/Apr 21 | K9-K12 | CNP-DNB | 1009 | 1014 | 1410 | 1415 | 4h06 | SMH/HSK |
| 112/Apr 21 | K13-K15 | DNB-NRD | 1505 | 1510 | 2000 | 2005 | 5h | SMH/HSK |
| 115/Apr 24 | K16-K19 KV Svalbard | NRD-DMH | 1004 | 1009 | 1442 | 1447 | 4h43 | SMH/HSK |
| 115/Apr 24 | K20-K23 | DMH-NRD | 1528 | 1533 | 1922 | 1927 | 3h59 | SMH/HSK |
| 118/Apr 27 | F | NRD-NRD | 1013 | 1018 | 1523 | 1528 | 5h15 | SMH/HSK |
| 119/Apr 28 | E | NRD-YLT | 1437 | 1442 | 1835 | 1840 | 4h03 | SMH/HSK |
| 120/Apr 29 | ICE | YLT-YLT | 1350 | 1355 | 1922 | 1927 | 5h37 | SMH/HSK |
| 122/May 1 | F-S | YLT-YLT | 1340 | 1345 | 1825 | 1830 | 4h50 | SMH/HSK |
| 122/May 1 | MYI-FYI | YLT-YLT | 1847 | 1852 | 2037 | 2042 | 1h55 | SMH/HSK |
| 123/May 2 | H | YLT-YLT | 1330 | 1335 | 1916 | 1921 | 5h51 | SMH/HSK |
| 123/May 2 | A1-FUE-A2 | YLT-YLT | 2040 | 2045 | 2308 | 2313 | 2h33 | SMH/HSK |
| 126/May 5 | M-cal-GM | YLT-THU | 1322 | 1327 | 1803 | 1808 | 4h36 | SMH/HSK |
| 127/May 6 | DEVON | THU-THU | 1154 | 1159 | 1703 | 1708 | 5h14 | SMH/HSK |
| 128/May 7 | DISKO | THU-SFJ | 1211 | 1216 | 1653 | 1658 | 4h47 | SMH/HSK |
| Total |  |  |  |  |  |  |  | 72h00 |

# Hardware Installation

The equipment was installed in the Twin Otter OY-POF in the Air Greenland hangar in Kangerlussuaq. The installation was similar to the setup certified in 2006 and used for the CryoVEx 2006 campaign. For this campaign a new laser scanner was used; the Riegl LMS Q240i. In addition the backup system consisting of a profiling laser altimeter and inertial measurement unit has been updated. Table 2 gives the offsets between the instruments and Figure 2 sketches the approximate position of the instruments in the aircraft.

Photographs of the installation are shown below.

Table 2. The (dx, dy, dz)’ offsets. The lever arm from the GPS antennas to the origin

of the laser scanner, and to the back centre of ASIRAS antenna frame (See arrow):

| to laser scanner | dx (m) | dy (m) | dz (m) |
| --- | --- | --- | --- |
| from AIR1/AIR3 (front) | - 3.70 | + 0.52 | + 1.58 |
| from AIR2/AIR4 (rear) | + 0.00 | - 0.35 | + 1.42 |
| to ASIRAS antenna | dx (m) | dy (m) | dz (m) |
| from AIR1/AIR3 (front) | -3.37 | +0.47 | +2.005 |
| from AIR2/AIR4 (rear) | +0.33 | -0.40 | +1.845 |

‘Offset definition: x positive to the front, y positive to the right, and z positive down.

Table 3. Data holding from aircraft instruments and reference stations

| JD/Date | AIR1 | AIR2 | AIR3 | AIR4 | ALT | EGI | IMU | SCAN-NER | GPS REF1 | GPS REF2 | GPS REF3 | Ver cam | ASIRAS | REMARKS |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 108/Apr 17 | X | X | X | X | n/a | ! |  | X | KELY |  |  | (X) | HAM+LAMa | Test flight, |
| 109/Apr 18 | X | n/a | X | X | X | ! | X | X | SFJ1 |  |  | (X) |  | Iceberg obs |
| 109/Apr 18 | n/a | X | X | X | X | ! | X | X | SFJ1 |  |  | X |  | Fjord trip for journ |
| 110/Apr 19 | X | X | X | X | X | ! | X | X | SFJ1 | JAV |  | X’’ | LAMa | Scanner PC cold no start |
| 110/Apr 19 | X’ | X | X | X | X | ! | X | X | SFJ1 | JAV | JUV | X’’ | LAMa | Pass over heli at 1620 |
| 111/Apr 20 | n/a | X | X | X | X | ! | X | X |  | CNP |  | X | HAM+LAMa | EGI difficult start up |
| 112/Apr 21 | X | X | X |  | X | ! | X | X | SCO | NYA2 |  | X’’’ | LAMa | EMAP probl with laptop |
| 112/Apr 21 | X | X | X |  | X | ! |  | X | SCO | NYA2 |  | X | LAMa | Changed survey lines |
| 115/Apr 24 | X | X | X |  | X | X | X | X | NRD1 | NRD2 |  | X | LAMa |  |
| 115/Apr 24 | X | X | X |  | X | X | X | X |  | NRD2 |  | X | LAMa |  |
| 118/Apr 27 | X | X | X |  | X | X | X | X | NRD1 | NRD2 |  | X | LAMa | Perfect weather… |
| 119/Apr 28 |  | X | X |  | X | X | x | X | THU3 | NYA |  | X | LAMa | IMU on late at 1707 |
| 120/Apr 29 |  |  | X |  | X | X | X | X | YLT1 | YLT2 |  | X | LAMa | CR on ice sheet |
| 122/May 1 | X | X | X |  | X | X | X | X | YLT1 | YLT2 |  | X | LAMa |  |
| 122/May 1 | X |  | X |  | X | X | X | X | YLT1 | YLT2 |  | X | LAMa | 4 CR on MYI and FYI |
| 123/May 2 | X | x | X |  | X | X | X | X | YLT1 | YLT2 |  | X | LAMa |  |
| 123/May 2 | X | X | X |  | X | X | X | X | YLT1 | YLT2 |  | X | LAMa | CR on site FUE, + heli |
| 126/May 5 | X | X | X |  | X | X | X | X | YLT2 | THU2 | THU3 | X | LAMa | Poor vis near YLT |
| 127/May 6 | X | X | X |  | X | X | X | X | THU2 | THU3 |  | X | LAMa |  |
| 128/May 7 | X | X | X |  | X | X | X | X | THU2 | THU3 | KELY | X |  | Disko in diff. alt. |

‘ stopped after end of survey line

‘’ not adjusted – images not clear – adjusted just after heli pass

‘’’ very cloudy

# Acquired data

During the CryoVEx 2008 campaign DTU Space acquired approximately 50 hours of ASIRAS data and 70 hrs of laser scanner, GPS, INS, and downward looking photographs with the airborne system. After each flight data was stored on dedicated harddisks and backup copies were made. The harddisks with ASIRAS data was delivered to AWI for processing. The remaining data was uploaded to the DTU Space servers also for post-processing.

An overview of the collected data can be seen in Table 3 and a more detailed description is found along with processing details in the following paragraphs.

Nearly all data were recovered and stored except for at few cases of operator errors, one laser scanner file never started and a few incidents where the GPS receivers had a full memory, but no problems were encountered for the main validation sites. The full set of raw data is now stored at the DTU space server system (with tape backup) and copies are kept on dedicated harddisks.

# Processing

## GPS data processing

Kinematic differential GPS is the key positioning method of the aircraft. GPS dual-frequency phase data were logged at 1 Hz using 1-2 ground base receivers at one or more reference sites, and 4 aircraft receivers; one of these dedicated to the ASIRAS system.

The aircraft GPS receivers are named AIR1 (Trimble 4000-SSI), AIR2 (Ashtech Z-extreme), AIR3 (Javad, Lexon), and AIR4 (Trimble 4000-SSI, connected to ASIRAS). AIR1 and AIR2 share the front GPS antenna; AIR3 and AIR4 the rear antenna. Antenna offsets are given in Table 2. Data were logged in the receivers during flights and downloaded upon landing on laptop PCs. Most data were recovered and only a few files missing, see Table 3, but the redundancy of receivers meant that GPS data are available for all flights. The AIR4 receiver had a problem with the serial port and was not downloaded after April 20.

The GPS base stations to be used as reference stations for differential post processing of the GPS data are listed in Table 4. The stations were mounted on roofs or tripods in the field near the landing sites; the reference points were generally not marked. In addition data from permanent GPS stations were used for data processing.

GPS solutions are based on static processing of the reference stations and kinematic differential processing of the airborne data. In addition precise point positioning has been used for some of the solution where precise information of satellite clock and orbit errors are used along with information from permanent IGS stations.

First the position of the reference station is determined using SCOUT (Scripps Coordinate Update Tool) service operated by SOPAC (Scripps Orbit and Permanent Array Center) (http://sopac.ucsd.edu). SCOUT calculates the reference positions in ITRF 2005 using data from three nearest permanent GPS stations with a position accuracy of about 2 cm even in the Arctic with long distance to permanent stations.

The reference stations used during CryoVEx 2008 are listed in Table 4 and coordinates are found in Appendix 8.3.

The kinematic differential GPS processing were performed with GPSurvey (version 2.35) using precise IGS orbits and the GOAD-Goodman tropospheric model. On each flight several solutions are made using different combinations of GPS reference stations and aircraft receivers. The best solution for each flight (see Table 6) is selected. For some of the flights GPSurvey showed to have problems delivering a stable solution and precise point positioning using the software Trip (X. Zhang 2006) gave a better solution and this was selected (*.kin in Table 6).

The GPS solution are used for further processing of INS and laser scanner data and also delivered to ESA and AWI for ASIRAS processing in the dedicated format documented by R. Cullen (2006).

Table 4. CryoVEx 2008 GPS reference stations

| Name | Location | Hardware (antenna type) |
| --- | --- | --- |
| SFJ1 | Kangerlussuaq, on met hut roof | Javad Maxor, (RegAnt) |
| JAV0 | On latter to roof, airport | Javad Maxor (int. ant, LegAnt) |
| JUV0 | Upernavik near airport | Javad Legacy (MarAnt) |
| CNP0 | On hotel roof | Javad Legacy (RegAnt) |
| NRD1 | Station Nord, on snow next to apron | Javad Maxor (int. ant) |
| NRD2 | Station Nord, on snow next to apron | Javad Legacy (RegAnt) |
| YLT1 | On snow next to Spinnaker, small tripod | Javad Maxor (int. ant) |
| YLT2 | Back side of Huricane, on stick | Javad Legacy (RegAnt) |
| THU2 | Thule Air Base, permanent station | Javad Legacy |
| THU3 | Thule Air Base, permanent station | Ashtech Z-XII3 |
| SCOR | Scoresbysund, permanent station | Ashtech UZ-12 |

## INS and GPS data merging

Similar to previous campaigns (e.g CryoVEx 2003, 04 and 06) a Honeywell medium grade inertial navigation system H764-G, EGI, was used throughout the surveys to record inertially integrated position, velocity and attitude information. Data were logged on a rack mounted PC with solid state hard-disks in binary format through a 1558 mil-spec communication bus. Data from all flights have been obtained. The data from April 17th to April 21st have not been initialised properly at the alignment but this will not affect the laser scanner processing as the files still contains the information needed about attitude changes. Recordings and comments can be found in Table 3.

The position and attitude information is extracted from the INS data packets and averaged to 10 Hz. The averaging to 10 Hz has proven to be a good balance between file size and resolution in time. To obtain a higher resolution in the time domain and preserve precision the post processed GPS and INS data is merged by draping the INS derived positions onto the GPS positions. This draping is done by modelling the function, found in equation (1), by a low pass smoothed correction curve, which is added to the INS.

ε (t) = PGPS(t) – PINS(t)			(1)

This way a smooth GPS-INS solution is obtained, which can be used for geolocation of laser and camera observation. The full resolution INS data were also converted into binary format as specified in the ESA document for the ASIRAS processing by R. Cullen (2006).

Details about the INS processing is found in Table 5 and Figure 4 shows an example of the draping of high rate INS heights onto precise GPS heights.

Figure 4. Draping of high rate INS derived heights (blue) onto precise GPS heights (red) to get high rate precise heights (black).

Table 5. GRL 2008 INS data processing

| JD | Flight | Filename | GPS solution | Start | Stop | Receiver |
| --- | --- | --- | --- | --- | --- | --- |
| 108 |  | gpsegi_108.pos | 108Air3.kin | 18.62 | 20.00 | 3 |
| 109 |  | gpsegi_109.pos | 109Air1.kin | 14.80 | 16.35 | 1 |
| 110 | a | gpsegi_110a.pos | 110aa4ja.p | 10.38 | 14.80 | 4 |
| 110 | b | gpsegi_110b.pos | 110ba2ja.p | 15.87 | 21.14 | 2 |
| 111 |  | gpsegi_111.pos | 111Air2.kin | 11.32 | 15.84 | 2 |
| 112 | a | gpsegi_112a.pos | 112aa3sc.p | 10.15 | 14.25 | 3 |
| 112 | b | gpsegi_112b.pos | 112bAir3.kin | 15.08 | 20.08 | 3 |
| 115 | a | gpsegi_115a.pos | 115aAir3.kin | 10.07 | 14.73 | 3 |
| 115 | B | gpsegi_115b.pos | 115bAir3.kin | 15.47 | 19.45 | 3 |
| 118 |  | gpsegi_118.pos | 118Air3.kin | 10.22 | 15.46 | 3 |
| 119 |  | gpsegi_119.pos | 119Air2.kin | 14.62 | 18.66 | 2 |
| 120 |  | gpsegi_120.pos | 120Air2.kin | 13.62 | 19.45 | 2 |
| 122 | a | gpsegi_122a.pos | 122aAir3.kin | 13.67 | 18.50 | 3 |
| 122 | b | gpsegi_122b.pos | 122ba3y2.p | 18.65 | 20.65 | 3 |
| 123 | a | gpsegi_123a.pos | 123aAir3.kin | 13.50 | 19.35 | 3 |
| 123 | b | gpsegi_123b.pos | 123ba2y2.p | 20.67 | 23.21 | 2 |
| 126 |  | gpsegi_126.pos | 126a3y2.p | 13.37 | 18.13 | 3 |
| 127 |  | gpsegi_127.pos | Air3gnav.p | 11.90 | 17.12 | 3 |
| 128 |  | gpsegi_128.pos | 128a1t3.p | 12.18 | 16.96 | 1 |

## Laser scanner data processing

The laser scanner system has been upgraded to the new Riegl LMS Q240i laser altimeter. This will provide similar measurements with near-infrared laser of the distance between the aircraft and the snow or ice surface as the old laser scanner previously used. The main difference is an improvement of the range; ranging up to 650 m over snow/ice and the smaller footprint; approximately 0.7x0.7 m at the nominal flying altitude of 300m.

The laser scanner data were logged as hourly files on a dedicated PC. The files are time-tagged by 1 PPS signal from the AIR1 GPS receiver and synchronised once per flight by the operator and named with the start time. Table 6 shows the logged files with start /stop times. The data rate has been fixed to 250 observations per line and 40 lines per second throughout the campaign.

The synchronisation of the data failed for part of the flights which means that the synchronisation has to be checked for each of these files during processing. This will not affect the data quality as it can be verified visually by plotting the results.

Laser scanner data were recovered for most flights except minor parts with low clouds or fog. Some problems occurred with the laser scanner PC at start up of the system caused by the cold weather. This was solved by heating the PC or running it during night on external power.

Figure 5. Sketch of laser scanner principle (1) Laser and photodiode assembly (2) Swath pattern (3) Rotating mirror.

The principle of the laser scanner can shortly be described as following:

1. The laser (1) emits a laser pulse and starts a timer, see Figure 5

2. The pulse is reflected in a direction dictated by the mirror (3)

3. If the pulse hits a target with suitable reflectance it is returned to the mirror (3) that reflects it into the photodiode (1) and hereby stops the timer

4 The mirror (3) is now rotated by a small angle before the process is repeated.

The geolocation of each point in the laser scanner data is performed with standard trigonometry in two steps. First all points are described as vectors (dXNWU, dYNWU, dZNWU) in a local Cartesian North East Up system using the lever arm between the laser scanner and the GPS (dX, dY, dZ), the range measured by the laser (r), the angle between the laser mirror (a) and the orientation of the laser in an earth fixed system (ωr, ωp, ωh). Next these vectors are added with the position derived from GPS (φGPS, λGPS, hGPS) to get the position of the reflector in an earth fixed system(φ, λ, h).

dXNWU =  cos(ωh)cos(ωp)dX

+ (cos(ωh)sin(ωp)sin(ωr) - sin(ωh)cos(ωr))(- sin(a)r + dY)

+ (cos(ωh)sin(ωp)cos(ωr) - sin(ωh)sin(ωr))(cos(a)r + dZ)

dYNWU =  - sin(ωh)cos(ωp)dX

-  (sin(ωh)sin(ωp)sin(ωr) + cos(ωh)cos(ωr))(- sin(a)r + dY)	(2)

+ (-sin(ωh)sin(ωp)cos(ωr) + cos(ωh)sin(ωr))(cos(a)r + dZ)

dzNWU =  sin(ωP) dX

- cos(ωp)sin(ωr)(- sin(a)r + dY)

- cos(ωp)cos(ωr)(cos(a)r + dZ)

φ = φGPS + dXNWU /degm

λ = λGPS + dYNWU /(degm cos(φ)				(3)

h = hGPS + dZNWU

where degm is meter per degree.

This geolocation process just described assumes perfect alignment between the laser scanner and the INS system, this is however not practically possible in this type of installation. To compensate for the imperfect installation several calibration manoeuvres are performed during the campaign. The purpose of these manoeuvres is to determine and monitor the offset angles between the laser scanner and the INS.

Figure 6. Laser scanner data from calibration site – building in Kangerlussuaq. Data from two passes overlaid displaying the match after calibration

The main calibration site for the laser is a building where the corners of the roof are known from a GPS survey. Using this building and two swaths of laser scanner data, one east-west and one north-south, one can estimate the offset angles through an iterative process. In Figure 6 points from the two swaths (heights in colour-coding) are plotted on top of the black outline of the building.

The calibration is monitored using similar methods over building (Station Nord and CFS Alert) and cross-overs during the surveys. Figure 7 shows the calibration flight at St. Nord on April 27.

Figure 7. Laser scanner data from the calibration flight at St. Nord.

Table 7 gives the processed laser scanner files with offset angles and other processing parameters. An example is shown in Figure 8 from the coincident flight with the AWI helicopter EM system on May 2nd and Figure 9 shows an overview of the delivered laser scammer data, colour coded separately for sea ice and ice caps. Note that the sea ice data has been filtered to heights relative to local sea level.

Figure 8. Example of laser scanner data over near the helicopter over-flight May 2nd.

Table 6. Processed laser scanner files

| JD | File name | Timing | Timing | Start (dechr) | Stop (dechr) | Calibration angl. |
| --- | --- | --- | --- | --- | --- | --- |
| 108 17/4-08 | GroundTest.2dd 108_185200.2dd | -1 |  | 18.83333 | 19.86874 | -1.5 0.20 0 |
| 109 18/4-08 | 109_154800.2dd | -1 |  | 15.53333 | 16.28035 | -1.5 0.19 0 |
| 110 19/4-08 | 110_105900.2dd 110_115430.2dd 110_130300.2dd 110_140000.2dd 110_155800.2dd 110_164700.2dd 110_174130.2dd 110_183300.2dd | 173 173 173 173 173 173 173 173 |  | 10.98333 11.90833 13.05000 14.00000 15.96667 16.78333 17.69167 18.55000 | 11.98568 13.03057 13.98347 14.73355 16.76490 17.67876 18.53849 19.41839 | -1.5 0.16 0 |
| 111 20/4-08 | 111_113715.2dd 111_121200.2dd 111_125700.2dd 111_140000.2dd | 176 176 176 176 |  | 11.62083 12.20000 12.95000 14.00000 | 12.18098 12.93720 13.98334 14.86993 | -1.5 0.16 0 |
| 112 21/4-08 | 112_101630.2dd 112_110900.2dd 112_115400.2dd 112_121300.2dd 112_134630.2dd 112_151530.2dd | 181 181 181 181 181 181 |  | 10.27500 11.15000 11.90000 12.21667 13.77500 15.25833 | 11.13432 11.74556 12.17062 12.68043 14.20751 15.98591 | -1.5 0.16 0 |
| 115 24/4-08 | 115_104200.2dd 115_113730.2dd 115_123500.2dd 115_122500.2dd 115_141630.2dd 115_153600.2dd 115_163330.2dd 115_174000.2dd | -1 -1 -1 -1 -1 -1 -1 -1 |  | 10.70039 11.62539 12.58377 13.41702 14.27542 15.60043 16.55869 17.66705 | 11.61595 12.57430 13.40475 14.26649 14.48988 16.54883 17.65387 18.81385 | -1.5 0.16 0 |
| 118 27/4-08 | 118_102000.2dd 118_112530.2dd 118_121530.2dd 118_131245.2dd 118_134830.2dd 118_142000.2dd 118_145900.2dd | -1 -1 -1 -1 -1 -1 |  | 10.33367 11.42543 12.25873 13.21292 13.80868 - 14.98377 | 11.41592 12.24841 13.18812 13.79712 14.31342 - 15.40674 | -1.5 0.19 0 |
| 119 28/4-08 | 119_144400.2dd 119_154000.2dd 119_163400.2dd 119_172430.2dd | -1 -1 -1 -1 |  | 14.73374 15.66705 16.56705 17.40874 | 15.65350 16.55936 17.39945 18.61004 | -1.5 0.19 0 |
| 120 29/4-08 | 120_135330.2dd 120_143930.2dd 120_161330.2dd 120_171400.2dd 120_175900.2dd 120_185615.2dd | -1 -1 -1 -1 -1 -1 |  | 13.89212 14.65883 16.22645 17.23375 17.98373 18.93793 | 14.64593 16.21969 17.22395 17.97291 18.92643 19.10401 | -1.5 0.19 0 |
| 122 1/5-08 | 122_134000.2dd 122_143500.2dd 122_153330.2dd 122_162730.2dd 122_173000.2dd 122_184630.2dd 122_193645.2dd | -1 -1 -1 -1 -1 -1 -1 |  | 13.66705 14.58370 15.55870 16.45869 17.50040 18.77561 19.61290 | 14.57000 15.55050 16.45018 17.48911 18.22298 19.60370 20.62406 | -1.5 0.19 0 |
| 123 2/5-08 | 123_133030.2dd 123_143100.2dd 123_151500.2dd 123_161500.2dd 123_172730.2dd 123_183830.2dd 123_204600.2dd 123_220030.2dd 123_230100.2dd | -1 -1 -1 -1 -1 -1 -1 -1 -1 |  | 13.50888 14.51708 15.25039 16.25038 17.45870 18.64210 20.76706 22.00874 23.02184 | 14.50900 15.24099 16.23944 17.44694 18.62964 19.29238 21.99410 22.86155 23.14300 | -1.5 0.19 0 |
| 126 5/5-08 | 126_131800.2dd 126_143400.2dd 126_145930.2dd | -1 -1 -1 |  | 13.30041 14.56704 14.99203 | 14.55898 14.98449 15.49834 | -1.5 0.19 0 |
| 127 6/5-08 | 127_120015.2dd 127_131200.2dd 127_133000.2dd 127_141600.2dd 127_150030.2dd | -1 -1 -1 -1 -1 |  | 12.00458 13.20036 13.50038 14.26708 15.00874 | 13.18491 13.49056 14.25457 14.99530 15.84995 | -1.5 0.19 0 |
| 128 7/5-08 | 128_121800.2dd 128_124515.2dd 128_134200.2dd 128_142630.2dd 128_151100.2dd | -1 -1 -1 -1 -1 |  | 12.30033 12.75456 13.70036 14.44210 15.18378 | 12.74411 13.68720 14.42977 15.17147 15.90188 | -1.5 0.19 0 |

Figure 9. Overview of delivered laser scanner data, colour coded separately for sea ice and ice caps. Note that the sea ice data has been filtered to heights relative to local sea level.

## ASIRAS radar data processing

The ASIRAS system was installed in the same manner as for the CryoVEx 2006 campaign. The new LAMa mode with reduced data rate was used for the surveys except for the CryoSat line near Ilulissat (April 20) where the HAM mode was used. The system was timed with PPS signal and ASCII datation string from the AIR4 Trimble GPS receiver.

Installation, ground test and test flight were performed with assistance from RST engineer H. Lentz in Kangerlussuaq. No problems occurred. The data were logged on the dedicated hard-disks in the ASIRAS PCs during flight and transferred to the PCs for backup after surveys. The data was backed up on hard-disk after the flights with a second copy on a spare set of disks.

Data were acquired continuously over the main sites and for parts of the other survey lines. The operator log files can be found in the Appendix together with a list of the recorded data files.

The data quality has been checked after each survey flight with the “Quicklook viewer” software from RST. Especially for the corner reflector sites the data were carefully checked. Examples can be found in the specific site descriptions, Section 5.

The final processing of the acquired ASIRAS data is done by the Alfred Wegener Institute (AWI) with input of GPS and INS position and attitude data from DTU Space.

Figure 10. ASIRAS processing scheme.

AWI AWI AWI…

## Auxilary data

During the survey flights operator logs were kept for both the DTU Space laser scanner and the ASIRAS radar system. These logs have been stored as separated files together with the data files and can also be found in the Appendix.

As backup for the laser scanner a profiling laser altimeter was installed next to the laser scanner and web camera. Also an extra inertial navigation unit was run as backup to the EGI instrument. These instruments were all timed by 1 PPS signals from GPS and data has been recorded on a dedicated PC and backed up post flight.

A downward looking web-camera was installed next to the laser scanner and operated during flights acquiring visual documentation of the surface. Images were captured every 2 seconds and time tagged using GPS. The image files were stored on a laptop PC during flight and backed up on hard-disk after each flight.

The images from the downward looking camera were triggered by GPS pulse via the IMU datation system. This means that a precise time (better than 10 msec) can be assigned to each image. Geolocation is done using the airplane position at the time of image acquisition.

An example is shown in Figure 11 from the over-flight of the AWI helicopter EM bird on May 2nd.

Figure 11. Image from downward looking camera of the helicopter over-flight on May 2nd 2008.

# Validation Sites

One of the main goals of the CryoVEx 2008 campaign was to gather coincident laser scanner and ASIRAS data over specific validation sites with scientist doing in-situ observations on the surface. At these sites corner reflectors were raised and the positions are listed in Table 7.

Table 7. CryoVEx  08 Corner Reflector Positions

| Name | Latitude (deg min sec) | Longitude (deg min sec) | Latitude | Longitude |
| --- | --- | --- | --- | --- |
| ICE2 | 79 0 0.919 N | 50 0 26.959 W | 79.0002555 | -50.0074887 |
| FYIE | 82 32 46.572 N | 62 34 50.880W | 82.54627 | -62.56808 |
| FYIW | 82 32 52.008 N | 62 35 8.340W | 82.54778 | -62.58565 |
| MYIS | 82 33 22.824 N | 62 33 33.696 W | 82.55634 | -62.55936 |
| MYIN | 82 33 36.540 N | 62 33 43.308 W | 82.56015 | -62.56203 |
| CAMP | 82 33 3.6 N | 62 34 30 W | 82.551 | -62.575 |
| DEVON | 75 20 17.124 N | 82 40 38.604 W | 75.33809 | -82.67739 |

Note: Several more CR was placed along the lines on Devon Ice Cap

More details about each validation site are found in the next paragraphs.

## Northern Greenland Ice Sheet - UK1

The UK1 team was positioned at the ice with the Air Greenland Twin Otter reg. OY-ATY from Thule Air Base. This “put-in” of the team was delay a few days caused by poor weather along the Greenland west coast but the UK team managed to be ready for the planned over-flight.

The UK1 site on the ice sheet was over-flown with the airborne laser and radar system on April 29. The reflector at the site (named ICE2) was passed from north and two times from east to west. The best hit of the reflector was the first pass from the north. Figure 2 shows a “Quicklook” image of the ASIRAS radar signal from the corner reflector at ICE2.

Thereafter the full transect was flown form ICE2 to ICE4 and the survey continued back to Alert over the Petermann glacier. Figure 13 shows the laser scanner elevations acquired near ICE2.

Figure 12. “Quicklook” image showing radar signal from the corner reflector at ICE2

Figure 13. Stacked laser scanner swaths of the over-flights of the ICE2 validation site April 29.

## Alert Sea Ice

The operations out of Alert focused on the validation sites near the coast on multiyear ice (MYI) and first year ice (FYI) and coordinated operations with the helicopter-borne EM bird system. In addition, longer surveys were carried out in the Arctic Ocean north-east and north-west of the station and a smaller survey near the AUV camp on the sea ice near Alert.

As describe in section 2 the flights were done on May 1st-2nd and May 5th. Figure 14 shows the details of the flight lines over the validation sites flown on May 1st. Both sites were over-flown repeatedly and in two altitudes 1000 ft and 1500 ft. At both sites two corner reflectors had been put up and these were hit more than once at each altitude.

Figure 14. Stacked laser scanner swaths from sea ice validation sites near Alert (heights are freeboards relative to the local sea level). Over-flight performed on May 1.

A coordinated flight with laser/radar from Twin Otter and EM from a helicopter was done in the afternoon on May 2nd. The helicopter was over-flown near the fuel cache laid out to enable a longer operation. The helicopter was definitely hit within the footprint of ASIRAS as it is clearly seen on the radar return, see Figure 15.

Figure 15. “Quicklook” image of helicopter over-flight on May 2nd. Note the reflection from both the helicopter itself and the EM bird below it

## Devon Ice Cap

The Devon site was surveyed on May 6th. It was planned to base the survey in the local settlement Grise Fiord but the weather did not favour this very small airfield and the base was moved to Thule Air Base. The main survey lines (E-W and N-S), see Figure 16, were observed twice to ensure good alignment over corner reflectors put up at the line crossing and at a handful other sites along the lines.

The reflectors were hit and also two additional lines were measured, as requested by the Canadian team on the Devon Ice Cap, before returning the aircraft to Thule.

Figure 16. Laser scanner swaths of the Devon Ice Cap survey on May 6th(colour coded heights relative to the WGS84 ell.). (In black: The planned lines – some on opportunity basis and not all observed)

## Others: Ilulissat and Fram Strait

On April 20th the EGIG line crossing the Greenland ice sheet between 70 and 72 N was surveyed. A line, similar to the future CryoSat tracks, was also flown on this flight over the inner part of Jakobshavn Isbræ near Ilulissat. This line almost heading N-S was measured both at high altitude (approx. 1100 m above the ice) in HAM mode and at 300 m in LAMa mode together with laser scanner observations (See Figure 9).

The Norwegian coastguard vessel KV Svalbard (see photograph) was on a scientific cruise for the Norwegian Polar Institute in April and May 2008. During the first part of the cruise the ship anchored to an ice floe in the Fram Strait between Greenland and Svalbard. Surface observations were done on this floe from the ship. A survey line on the floe was over flown with the airborne system on April 24th together with sea ice observations on east-west lines along the Greenland coast. The sea ice team on KV Svalbard also erected a corner reflector on the line but it was not hit with the ASIRAS. Figure 18 shaws the laser scanner data, note the sea ice motion between over-flights.

Figure 17. KV Svalbard in the Fram Strait (77N25, 7W22) on April 24th 2008

Figure 18. Laser scanner data from the KV Svalbard over-flight. Note that the sea ice has moved significantly during the survey (the crossing track has been observed last).

# Conclusions

The airborne part of CryoVEx 2008 has successfully been carried out by DTU Space and the gathered data sets are now secured at DTU Space on central servers backed up on magnetic tapes. A total of 72 hr were flown with the Air Greenland Twin Otter plus additional 15 hrs for the transport of the UK1 team to the ice sheet. Laser scanner data has been gathered on most lines and ASIRAS data was recorded over test sites and on large parts of the other lines.

The laser scanner, INS, and GPS data has been processed by DTU Space and the ASIRAS data by AWI.

# References

Cullen, R.: ASIRAS, Product Description, Issue: 2.5. European Space Agency, 2007

Haas, C, S. Hanson, S. Hendricks: CryoVEx 2008 Field report of in-situ measurements, 2008

Helm, V., S. Hendricks, S. Goebell, W. Rack, C. Haas, U. Nixdorf, and T. Boebel: CryoVEx 2004 and 2005 (bob) data acquisition and final report. Technical Report 1.0, Alfred Wegener Institute, 2006.

Zhang, X.: Precise Point Positioning – Evaluation and Airborne Lidar Calibration. Technical Report No. 4, Danish National Space Center, pp. 44, 2006.

# Appendix

## Operator logs

Operator logs for laser scanner system (left) and ASIRAS (right). Track plots also shown:

JD 108 17/4-08 SFJ-drop-test-SFJ

1842	Take off

185200?	New scanner file

Tent dropped on the ice

Climb to 6000ft

Decent to approx. 900m

Decent slowly to 1000ft in fjord

Return at 1000ft

1941	Over blue building 1

Cross over building at 1000ft

1955	Landing

Asiras CryoVEx 2008

JD 108 - 17 04 08

SFJ -> SFJ testflight

2038 take off

2155 landed

JD 109 18/4-08 SFJ-ICB-JAV

1453	Take off

Image capture off for adjusting

153200	Scanner sync

No power on Air2 cable remounted

1541	Air2 restarted

154800	New scanner file, +1sec?

1556	ICB1; Alt 230m/800ft

Deviate line to obs icebergs

1616	Landing

JAV-fjord-JAV for journalists

1758	Taxi

1801	Take off

180800	Scanner sync

180953	New scanner file, file name 181000

Started 181057

1818	Turn over Isbræ edge

1828	IMU restart logging

1835	Landing

Asiras CryoVEx 2008

JD 109 - 18 04 08

JAV -> JAV flight for DR journalists

1800 take off

1802 system on

1807 IRF calibration

1810 LAM mode

1812 record on (sea ice)

1818 record off (turn)

1820 record on

1825 record off

1827 record on

1830 record off

1830 IRF calibration

1834 system off

1835 landed

JD 110 19/4-08 JAV-K-JUV-HELI-K-JAV

Scanner pc down – too cold

Try to shift to laptop not ok

1028	Take off

Pass over runway for journalists

103500	Scanner sync, scanner start no signal

problem with logging on Lars’ pc

104600	Scanner sync

105700	Scanner sync, scanner pc up

105900	New scanner file

1104	Image capture started

1120	Xtra monitor tested ok

Some clouds JAV-K1

1147	K1

115430	New scanner file

1300	K2, tear drop turn

130300	New scanner file

1326	K3, direct turn

140000	New scanner file

1419	K4, open water and thin ice

1443	Landing JUV

Asiras CryoVEx 2008

JD 110 - 19 04 08

JAV -> UPERNAVIK

1032 system on

1035 IRF calibration

1058 record on (test)

1103 record off

1145 record on (sea ice)

1220 record off

1220 record on

1255 record off (turn)

1300 record on

1325 record off (turn)

1328 record on

1407 record off

1407 record on

1419 record off (turn)

1424 IRF calibration

1425 system off

Coordinate with helicopter

1510	Take off helicopter

Download 1st part

1557	Take off

155800	New scanner file

1604	HE2

1616	HE5

1620	HE6, overflight of heli on ground

Perfectly coordinated

1633	Light fog

164700	New scanner file

1721	K6, tear drop turn

174130	New scanner file

1800	K7

183200 (183300?) New scanner file

1856	K8, end of line

Obs of icebergs

1922	Start climb

1925	Stop logging scanner + alt

Stop logging Air1 to download

2108	Landing

UPERNAVIK -> JAV

1601 system on

1603 IRF calibration

1605 record on (thin sea ice)

1620 overhead helicopter

1635 record off

1635 record on

1705 record off

1705 record on

1721 record off (turn)

1724 record on

1745 record off (switch to PC2)

1746 record on

1758 record off (turn)

1759 record on

1830 record off

1830 record on

1855 record off (turn)

1856 record on

1923 record off

1924 IRF calibration

1927 system off

JD 111 20/4-08 JAV-EGIG-CNP

Hard to start up EGI

Perhaps Air1 was started after EGI

No lock on sat, fixed height align

1113	NavRdy finally

1115	Engine start up

1125	Take off

11??	Scanner sync

113718	New scanner file called 113715

JAV line 1-10, 1000ft south

1150	JAV5 1st time, some low clouds

1156	Return north, aprox 1100m above ice

121200	New scanner file

121230	JAV10, decent to 1000ft

1223	T1

1227	T3

123130	T5

125700	New scanner file

140000	New scanner file

1452	Scanner file closed

1548	Landing CNP

Asiras CryoVEx 2008

JD 111 - 20 04 08

JAV -> CNP

1130 system on

1132 IRF calibration

1135 record on

1142 record off

1144 record on

???? record off

12?? record on (HAM)

1213 record off

1215 record on (LAM)

1246 record off

1246 record on

1313 record off

1313 record on

1330 record off

1330 record on

1400 record off

1400 record on

1430 record off

1430 record on

1451 record off

1455 IRF calibration

1458 system off

JD 112 21/4-08 CNP-K-DNB-Krev-NRD

Scanner sync on ground

Pobl with EMAP start up

Perhaps problems with seriel port on laptop

1000	Engine start

1010	Taxi

1014	Take off

101630	New scanner file

1030	EMAP up on smh laptop

1040	Decent to 1000ft

1045	End of fast ice

110900	New scanner file

1115	K9 tear drop turn

1123	Low clouds

1130	Climb to 460m

1144	Scanner file closed

115400	New scanner file (start 04)

Clouds partly broken

1201	Decent, try to get under clouds

1204	Icing, climb

1220	Broken clouds, 660m alti, some scanner

1228	K10, 750m, only ASIRAS

1238	800m

1254	K11, clouds, only little sea ice

134630	New scanner file still in clouds

1358	K12

1407	Overflight runway DNB

ASIRAS log: 21/4-2008, JD 112:

Operator: HSK

Flight: CNP-DNB, DNB-NRD:

Take off Constable Pynt

1116 	start log file A080421_00, flight altitude 300m

1130 	Ascend to 480m

1142 	Ascend to 540m

1200 	Descend to 300m

1203 	new log file A080421_01

Climb to 660m

1222	climb to 720m

1227	turn – stop logging

1254	new log file A080421_02

1301	climb to 900m

climb to 960m

1309	descend to 900m

1311	descend to 840m

1333	descend to 660m

1337	descend to 540m

1340	descend to 420m

1350	descend to 360m

1309	descend to 300m

1356	stop logging

1357	calibration

Landing Daneborg

1410	Landing DNB

Fueling, 1 engine running for instruments

1507	Taxi

1510	Take off

1540	After Shannon Island in fog again

1610	Deviate line, direct north

163130	New scanner file

1634	1000ft, turn towards K15

1642	Long leads and large patches without leads

1723	K15, turn direct towards NRD

172500	New scanner file

181400	New scanner file fog/low clouds – some broken

1843	Scanner logging stopped

185900	New scanner file

1935	Flade isblink start

2000	Landing NRD

Take off Daneborg

1533	new log file A080421_03, 300m

1544	climb to 600m

1601	new log file A080421_04

1615	new log file A080421_05

1635	new log file A080421_06

1652	new log file A080421_07, 300m

1714	new log file A080421_08

1721	turn

new log file A080421_10

1735	new log file A080421_11

1749	new log file A080421_12

frostflowers

1812	PC1 full change to PC2

new log file A080421_13

1829	new log file A080421_14

1843	new log file A080421_15

1859	new log file A080421_16

1914	new log file A080421_17

1929	stop radar

Calibration

Shut down system

Landing St. Nord

JD 115 24/4-08 NRD-K-KV Svalbard-DMH-K-NRD

Problems with scanner start up

PC restarted several times – without scanner on

Connected but no data in

1000	Taxi

1009	Take off

Scanner restarted 1000 times, check of net-connection

Finally receives data + sync

104200	New scanner file

1047	Image capture started

1130?	EGI input stopped, program restarted

1135	K20, turn

113730	New scanner file

1233	K21

123500	New scanner file

1248	KV Svalbard, 77 25N 7 22W, VHF 130.5

200 m line east of ship

1300	Overhead KV Svalbard

1322	3 passes and overhead ship into line

132500	New scanner file

141630	New scanner file, end of line

1442	Landing DMH

6 drums of fuel

ASIRAS log: 24/4-2008, JD 115:

Operator: HSK

Flight: NRD-KV Svalbard-DMH, DMH-NRD:

0830	Take off NRD

1015	ASIRAS startup, int. calibration

1019	Ready

1136	new log file A080424_00, 300m

1150	new log file A080424_01

1205	new log file A080424_02

1220	new log file A080424_03

1233	log stopped, turn

1235	new log file A080424_04

1250	new log file A080424_05

1259	new log file A080424_06

1300	KV Svalbard

1303	stop file

1304	new log file A080424_07

1307	KV Svalbard

1309	stop log file

1310	new log file A080424_08

1312	KV Svalbard

1314	stop log file

1315	new log file A080424_09

13	KV Svalbard

1319	stop log file

1323	new log file A080424_11

1333	new log file A080424_12

1344	new log file A080424_13

1355	new log file A080424_14

1405	new log file A080424_15

1415	new log file A080424_16

1417	stop file

1418	stop radar, int. calibration

Landing DMH

EGI restarted and aligned

153045	Taxi

1533	Take off

153600	New scanner file

1553	Air1 start logging

1612	Image capture restarted

163330	New scanner file

1652	K21, tear drop turn

170620	End of fast ice

1718	Some clouds

1738	K22, direct turn

174000	New scanner file

1808	K23

1848	End of line, K24

Scanner file closed

1922	Landing

Take off DMH

1541	ASIRAS startup, int. calibration

1556	test PC1 55% A080424_18

1655	new log file A080424_19

1705	new log file A080424_20

1716	new log file A080424_21

clouds

1725	new log file A080424_22

1735	new log file A080424_23

1737	stop file

1808	new log file A080424_24

1818	new log file A080424_25

1828	new log file A080424_26

1838	new log file A080424_27

1847	stop file

1848	stop radar, int. calibration

Landing NRD

JD 118 27/4-08 NRD-F-NRD

Problems with scanner start up

PC lost all settings

100230	Scanner sync

1006	Engine start

1013	Taxi

1018	Take off

1020	New scanner file

103430	End of fast ice

1040	Large lead

1124	Start new line after F1 tear drop turn

112530	New scanner file

1159	Image capture restarted

Scanner logging stopped?

121530	New scanner file

131245	New scanner file

1312	F2 tear drop turn

Scanner logging slow, stopped again

134830	New scanner file

142000	New scanner file – logging never started!

143640	Large open lead, shear zone

Very thick fast ice edge

145900	New scanner file

1505	Runway pass

1509->	Building over-flight

1523	Landing

ASIRAS log: 27/4-2008, JD 118:

Operator: HSK

Flight: NRD-trekant-NRD:

Take off NRD

1018	startup system

1020	int. calibration

1026	new log file A080427_01

1035	new log file A080427_02

1045	new log file A080427_03

1059	new log file A080427_04

1110	new log file A080427_05

1116	stop log file, teardrop

1120	new log file A080427_06

1130	new log file A080427_07

1140	new log file A080427_08

1151	new log file A080427_09

1200	new log file A080427_10

1210	new log file A080427_11

1220	new log file A080427_12

1230	new log file A080427_13

1242	new log file A080427_14

1300	new log file A080427_15

1308	stop log file, teardrop

1313	new log file A080427_16

1325	new log file A080427_17

1335	new log file A080427_18

1346	new log file A080427_19

1358	new log file A080427_20

1410	new log file A080427_21

1425	new log file A080427_22

1432	refrozen lead

1435	new log file A080427_23

1445	new log file A080427_24

1455	new log file A080427_25

1458	new log file A080427_26

1502	overflight runway NRD

1503	stop log files

1505	new log file A080427_27

1505	turn

1507	overflight building NRD

1508	stop log file

1508	new log file A080427_28

1510	stop log file

1511	new log file A080427_29

1514	overflight building NRD

1515	stop log file

1516	new log file A080427_30

1517	overflight building NRD

1518	stop log file, int. calibration

Landing NRD

JD 119 28/4-08 NRD-E-YLT

Problems with IMU start up

No network connection, no data in

142300	Scanner sync

1439	Taxi

1442	Take off

144400	New scanner file

1458	E3

150430	ALT restarted, IMU still off

R4-R1 (off E3-E2 at 1512)

153130	Back on E3-E2 shear zone, lead

154000	New scanner file

1554	T4-T1

1558	T1-S4 over glacier

1607	S4-S1

161245	Fast ice edge

161650	E2

163400	New scanner file

163740	E1, tear drop turn

1704	ALT stop logging, try to restart IMU by power off

1707	IMU+ALT restarted!

172430	New scanner file

1835	Landing

ASIRAS log: 28/4-2008, JD 119:

Operator: HSK

Flight: NRD-YLT

1442	Take off NRD

1621	ASIRAS startup, int. calibration

1625	new log file A080428_00, test

1638	new log file A080428_01

1651	new log file A080428_02

1700	new log file A080428_03

1710	new log file A080428_04

1720	new log file A080428_05

1731	new log file A080428_06

1737	open lead, event mark 1

1740	new log file A080428_07

1751	new log file A080428_08

1756	FY ice

1800	new log file A080428_09

1810	new log file A080428_10

1812	rubled ice, pix 215/216

1813	FYI

1820	new log file A080428_11

1826	stop file

1827	int. calibration, shut down system

Landing YLT

JD 120 29/4-08 YLT-ICE-A-YLT

Scanner PC too cold

Problems with scanner PC connection

PC restarted several times

134000	Scanner sync

1352	Taxi

135330	New scanner file

1355	Take off

143930	New scanner file, start of ice sheet

154400	CR from north ~0m

155330	CR from east ~10m

160210	CR from east ~15m

161040	CR from east ~-13m

161330	New scanner file (started 161334)

1618	CR from east ~-25m

Continue on line to ICE3

1641	ICE3

1710	ICE4

171400	New scanner file

1744	A2

175900	New scanner file

1800	A3

1844	End of glacier

184730	A5

185615	New scanner file

1922	Landing

ASIRAS log: 29/4-2008, JD 120:

Operator: HSK

Flight: YLT-ICESHEET-PETERMAN GL.-YLT

Take off YLT

1355	ASIRAS startup, int. calibration

1439	new log file A080429_00, 240m

1440	climb to 300m

1449	new log file A080429_01

1459	new log file A080429_02

1509	new log file A080429_03

1520	new log file A080429_04

1530	new log file A080429_05

1540	new log file A080429_06

1544	stop log file, tear drop

1551	new log file A080429_07

15535	reflector, event mark 1

1554	stop log file

1600	new log file A080429_08

1602	stop log file

1608	new log file A080429_09

1611	stop log file

1616	new log file A080429_10

1626	new log file A080429_11

1636	new log file A080429_12

1646	new log file A080429_13

1656	new log file A080429_14

1708	end of line, stop log file

1714	new log file A080429_15

1725	new log file A080429_16

1735	new log file A080429_17

1744	end of line, stop log file

1745	new log file A080429_18

1759	end of line, stop log file

1800	new log file A080429_19

1810	new log file A080429_20

1820	new log file A080429_21

1832	new log file A080429_22

1841	new log file A080429_23

1844	event marker 1, end of glacier

1852	new log file A080429_24

1900	new log file A080429_25

Climbing to 1020m

1906	stop file, internal calibration

Shut down system

Landing YLT

JD 122 1/5-08 YLT-F-S-YLT-MYI-FYI-YLT

Problems with POF HF radio

1331	EGI logging restarted (program restarted)

133530	Scanner sync

134000	New scanner file, still on ground

1343	Taxi

1345	Take off

143500	New scanner file

1437	F3

153330	New scanner file

1547	F2, tear drop turn

162730	New scanner file

Loose connection in power in to rack,

running on batteries for a while, look out for the plug

173000	New scanner file

1807	End of line

1825	Landing

ASIRAS log: 1/5-2008, JD 122:

Operator: HSK

Flight: YLT-triangle-YLT, YLT-MYI-FYI-YLT

Take off YLT

1350	ASIRAS startup, int. calibration

1352	new log file A080501_00, 300m

1402	new log file A080501_01

1412	new log file A080501_02

1422	new log file A080501_03

1433	new log file A080501_04

1437	stop log file, end of line

1445	new log file A080501_05

1456	new log file A080501_06

1505	new log file A080501_07

1515	new log file A080501_08

1526	new log file A080501_09

1535	new log file A080501_10

1547	stop file, teardrop

1551	new log file A080501_11

1600	new log file A080501_12

1610	new log file A080501_13

1620	new log file A080501_14

1630	system down, power failure

1642	start up, int. calibration

1643	new log file A080501_15

1655	new log file A080501_16

1705	new log file A080501_17

1715	new log file A080501_18

1725	new log file A080501_19

1736	new log file A080501_20

1746	new log file A080501_21

1756	new log file A080501_22

1807	stop file

1808	int. calibration, shut down

On ground YLT

Pick up MD

1000ft over CR and then 2000ft

183630	New scanner file

1850	Taxi

1852	Take off, heading towards MY

185920	CR ~30-40m

190945	CR ~4m

191730	CR ~-6m, from south

192630 	CR ~-1m

Climb to 2000ft

1934	CR ~0m!

193645	New scanner file

194210 	CR ~-3m

195150	Crossing runway, heading for FYI

195310 	CR ~10m

200127 	CR ~-2m

Decent to 1000ft

200240 	Crossing runway

200828	Crossing runway

200950 	CR ~-5m

2017 	CR ~6m

2025 	CR ~3m

203225 	CR ~6m

2037	Landing

Take off YLT

1854	turn on system, int. calibration

1858	new log file A080501_23, PC2

MYI S → N 1,000ft

1901	stop file

190551 	new log file A080501_24

MYI N → S 1,000ft

1911	stop file

191523 	new log file A080501_25

191730	MYI S → N 1,000ft

1919	stop file

192302 	new log file A080501_26

192630	MYI N → S 1,000ft

1927	stop file

Climb to 2,000ft

193120 	new log file A080501_27

193400	MYI S → N 2,000ft

193536	stop file

193915 	new log file A080501_28

194206	MYI N → S 2,000ft

194315	stop file

194945 	new log file A080501_29

195248	FYI E → W 2,000ft

195456	stop file

195832 	new log file A080501_30

200127	FYI W → E 2,000ft

200145	stop file

Descend to 1,000ft

200636 	new log file A080501_31

200945	FYI E → W 1,000ft

201134	stop file

201426 	new log file A080501_32

201710	FYI W → E 1,000ft

201812	stop file

202205 	new log file A080501_33

202457	FYI E → W 1,000ft

202619	stop file

202925 	new log file A080501_34

203204	FYI W → E 1,000ft

203234	stop file

2033	int, calibration, shut down system

Landing YLT

JD 123 2/5-08 YLT-H-YLT-A-FUE-A-YLT

Problems with scanner PC start up

132800	Scanner sync

133030	New scanner file

1335	Take off

Local patches of fog

143100	New scanner file

1500	H1

151500	New scanner file, fog

1608	H3

161500	New scanner file

1720	Air2 stopped logging, card full, restarted

1720	H5

172730	New scanner file

1747	H6

1837	H7

183830	New scanner file

1916	Landing

Fuel

New start up

Coincident flight with helicopter

2020	Heli take off

202800	Scanner sync

2045	Take off

204600	New scanner file

2105	A1 after turn to align on track

2127	FUE ~0m

2126	Heli over-flight

21??	Air1 stop logging, disc full

215905	A2

220030	New scanner file

220310	A2

223058	FUE ~6m, heli on ground

2251	A1, end of survey line

Low level in to YLT

2308	Landing

ASIRAS log: 2/5-2008, JD 123:

Operator: HSK

Flight: YLT-H-YLT, YLT-A1-A2-A1-YLT

Take off YLT

1336	ASIRAS startup

1343	int. calibration

1344	new log file A080502_00, 300m

1355	new log file A080502_01

1405	new log file A080502_02

1415	new log file A080502_03

1425	new log file A080502_04

1435	new log file A080502_05

1445	new log file A080502_06

1455	new log file A080502_07

1501	stop file, end of line

1518	new log file A080502_08

1530	new log file A080502_09

1540	new log file A080502_10

1550	new log file A080502_11

1600	new log file A080502_12

1608	stop log file, end of line

1626	new log file A080502_13

1636	new log file A080502_14

1645	new log file A080502_15

1655	new log file A080502_16

1705	new log file A080502_17

1715	new log file A080502_18

1722	stop file, end of line

1751	new log file A080502_19

1800	new log file A080502_20

1810	new log file A080502_21

1820	new log file A080502_22

1830	new log file A080502_23

1837	stop line

1840	int. calibration

Landing YLT/Take off YLT

2045	system startup

2050	int. calibration

2051	new log file A080502_24, test

2058	new log file A080502_25 (NW)

2100	stop log file

210525	new log file A080502_26, A1

2115	new log file A080502_27

212500	new log file A080502_28

212643	reflector, helicopter

213500	new log file A080502_29

214500	new log file A080502_30

215500	new log file A080502_31

215915	stop log file, A2

220240	new log file A080502_32

221200	new log file A080502_33

222200	new log file A080502_34

222700	new log file A080502_35

223058	over airstrip, fuelcache

223700	new log file A080502_36

224700	new log file A080502_37

225126	stop log file, end of survey

2252	int. calibration, shut down

On ground YLT

JD 126 5/5-08 YLT-M-cal-GM-THU

Scanner PC reconnected

Power loss on ground cable

Restart with engine on

Scanner sync

130700	New scanner file, on ground

Start with Mow-the-lawn

1327	Take off

Poor visibility, change alt to 200m

Only chose central lines and add more close to camp

+-150m of camp approx.

1416	End of survey lines E-W

1420	Start calib over Spinnaker

1432	End of calib

143400	New scanner file, up through clouds

Heading for GM1-GM8

145930	New scanner file

152930	GM8, end of survey

1803	Landing

ASIRAS log: 5/5-2008, JD 126:

Operator: HSK

Flight: YLT-AUV-ice on Ellesmere Island-THU

Take off YLT

1327	ASIRAS startup

1333	int. calibration

133455	new log file A080505_00, 300m

AUV M1-M2

1338	stop file, end of line

134644	new log file A080505_01, 240m

135108	stop file, end of line

AUV M5-M6

135510	new log file A080505_02, 240m

135928	stop file, end of line

AUV M7-M8

140314	new log file A080505_03, 240m

AUV

140745	stop file, end of line

141241	new log file A080505_04, 240m

AUV

141708	stop file, end of line

142009	new log file A080505_05

Overflight Runway+Spinaker building YLT

142105	stop file

142308	new log file A080505_06

Overflight Spinaker

142400	stop file

1426	new log file A080505_07

Overflight Spinaker

142740	stop file

143030	new log file A080505_08

Overflight Spinaker

143208	stop file

144930	new log file A080505_09*

145939	stop file

151140	new log file A080505_10*

152100	new log file A080505_11*

1529	stop file

1533	int. calibration, shut down system

Landing Thule AB

* Survey on Ellesmere Island, various heights due to changing surface heights.

JD 127 6/5-08 THU-DEVON-THU

Normal start up with engine on

114500	Scanner sync

1159	Take off

120015	New scanner file

1225	EMAP restarted Cy1, Cy5 deleted

Too close to CR

131200	New scanner file

133000	New scanner file

1336	45_4 ~6m

CR ~18m

1345	End of 45_1-45_10

1401	62_2 after tear drop turn into line

CR ~17m

140830	Cy10 ~-4m

Cy19 ~-8m

141600	New scanner file

Repeat 45_1-45_9

142440	45_1, start line

1428	45_4 ~12m

CR ~-20m

1440	N-S line repeated

1447	CR ~-2m

1456	Cy45, turn towards NSw1

150030	New scanner file

150250	NSw1

1514	NSw4, turn towards NASA line

1524	NA2

1547	NA7, end of line

1550	End of survey, scanner logging off

Direct THU

1703	Landing

ASIRAS log: 6/5-2008, JD 127:

Operator: HSK

Flight: THU-Devon icecap-THU

Take off THU

1202	ASIRAS startup

1204	int. calibration

1205	new log file A080506_00, 300m

1222	new log file A080506_01

1232	new log file A080506_02

1242	new log file A080506_03

1252	new log file A080506_04

1302	new log file A080506_05

1312	new log file A080506_06

1318	stop file

Devon icecap

133228	new log file A080506_07

133745	reflector/camp

134534	stop file, end of line

140047	new log file A080506_08, 420m

140115	300m

140656	reflector

140820	360m

140838	300m

141109	stop file

142408	new log file A080506_09

143009	camp/reflector

143102	stop file

144128	new log file A080506_10, 480m

144258	360m

144346	300m

144747	reflector

145208	360m

145225	300m

145628	PC1 record stopped

1457	new log file A080506_11, test

1458	new log file A080506_12, test

Stopped again

1459	change to PC2

1500	new log file A080506_13, test

1501	stop file - OK

150305	new log file A080506_14

1506	try 360m back to 300m

151425	stop file

152330	new log file A080506_15, 420m

152358	360m

152425	300m

153130	new log file A080506_16

153500	camp on starboard

154100	new log file A080506_17, 300m

154240	360m

154340	420m

154724	stop file, end of survey

1548	int. calibration

1550	shut down system

Landing Thule AB

JD 128 7/5-08 THU-DISKO-SFJ

Normal start up with engine on

120000	Scanner sync

1204	IMU+ALT restarted, IMU input stopped

1207	Taxi

1216	Take off

121800	New scanner file

1228	EMAP restarted – new map on screen

124515	New scanner file

Melville Bay open water in northern part

134200	New scanner file

142630	New scanner file

151100	New scanner file

1552	End of Disko survey

Direct SFJ

1653	Landing

## File formats

The file format description for the core products can be found in “ASIRAS, Product Description, Issue 2.5” by R. Cullen (2007) and the user should refer to this document for a detailed description, Especially concerning the ASIRAS products which are not discussed in the following. The definition of the types used in the binary files can be found in Table 8.

Table 8. Definition of binary types used in the description of the file formats.

Processed DGPS data is delivered in binary, big endian format with each record formatted as described in Table 9.

Table 9. GPS file format.

The processed INS data is delivered in binary, big endian format with each record formatted as described in Table 10.

Table 10. INS file format.

The processed laser scanner data is delivered in binary, little endian format with each record formatted as described in Table 11. Note that the time is decimal hours since the beginning of the day with respect to UTC time.

Table 11. Laser scanner file format.

## GPS reference coordinates

Reference GPS station coordinates in ITRF 2005.

Table 12 GPS reference coordinates

| Name | Day | Lat (DMS) | Lon (DMS) | Ellipsoidal Height (m) |
| --- | --- | --- | --- | --- |
| SFJ1 | 109 | 67 0 21.6428 | -50 42 9.7167 | 71.8670 |
|  | 110 | 67 0 21.6429 | -50 42 9.7166 | 71.8663 |
|  | 131 | 67 0 21.6429 | -50 42 9.7167 | 71.8626 |
|  | 134 | 67 0 21.6430 | -50 42 9.7169 | 71.8605 |
|  | 135 | 67 0 21.6429 | -50 42 9.7168 | 71.8675 |
|  | 133 | 67 0 21.6430 | -50 42 9.7167 | 71.8573 |
| SCOR | 111 | 70 29 7.1998 | -21 57 1.2123 | 128.4871 |
| NRD1 | 115 | 81 35 47.4178 | -16 39 50.9411 | 61.4741 |
|  | 118 | 81 35 47.3958 | -16 39 51.5421 | 61.8364 |
| NRD2 | 118 | 81 35 47.7708 | -16 39 51.2947 | 62.0200 |
| YLT1 | 120 | 82 30 40.1035 | -62 19 7.8670 | 44.0638 |
|  | 122 | 82 30 42.1338 | -62 19 56.2566 | 51.6529 |
|  | 123 | 82 30 42.1340 | -62 19 56.2577 | 51.6501 |
| YLT2 | 120 | 82 30 39.5054 | -62 19 13.9806 | 45.3253 |
|  | 122 | 82 30 39.5053 | -62 19 13.9794 | 45.3350 |
|  | 123 | 82 30 39.5053 | -62 19 13.9793 | 45.3347 |
|  | 126 | 82 30 39.5053 | -62 19 13.9805 | 45.3381 |
| JAV0 | 110 | 69 14 25.3716 | -51 3 56.7004 | 58.9223 |
| JUV0 | 110 | 72 47 16.2809 | -56 7 45.1428 | 159.0137 |

Mean values used for processing:

Lat	Lon	E. Height

SFJ1		67  0 21.6429	-50 42  9.7167	71.8635

NRD1		81 35 47.4068	-16 39 51.2416	61.6552

YLT1 (120+122+123)	82 30 41.4571	-62 19 40.1271	49.1223

YLT1 (122+123)	82 30 42.1339	-62 19 56.2572	51.6515

YLT2		82 30 39.5053	-62 19 13.9799	45.3333

## Corner reflector details from sea ice in-situ observations

Details of corner reflectors on the sea ice near CFS Alert:

See also the field report from the ground validation work by Haas, Hanson, and Hendricks, CryoVEx 2008 Field report of in-situ validation measurements, 2008.

## ASIRAS data files

List of recorded ASIRAS files with start/stop times, range window and number of pulses: (or processed ASIRAS files)

Table13. Recorded ASIRAS files

| File name [AYYMMDD] | Start time | Stop time | Range Window [m] | # Pulses |
| --- | --- | --- | --- | --- |
| A080417_00.log | 16:02:40 | 16:02:45 | 18.00 | 5783 |
| A080417_01.log | 16:04:14 | 16:04:19 | 90.00 | 9419 |
| A080417_02.log | 16:06:56 |  | 90.00 |  |
| A080417_03.log | 16:09:30 | 16:09:36 | 18.00 | 7500 |
| A080417_04.log | 21:13:03 | 21:15:12 | 18.00 | 375148 |
| A080417_05.log | 21:24:23 | 21:26:44 | 90.00 | 347498 |
| A080417_06.log | 21:28:37 | 21:30:33 | 90.00 | 284998 |
| A080417_07.log | 21:33:09 | 21:36:15 | 90.00 | 459998 |
| A080418_00.log | 20:07:07 | 20:13:34 | 90.00 | 1152455 |
| A080418_01.log | 20:15:45 | 20:21:31 | 90.00 | 1032407 |
| A080418_02.log | 20:22:29 | 20:25:12 | 90.00 | 483191 |
| A080419_00.log | 12:52:16 | 12:58:17 | 90.00 | 1074424 |
| A080419_01.log | 13:40:34 | 14:15:01 | 90.00 | 6194438 |
| A080419_02.log | 14:15:02 | 14:49:44 | 90.00 | 6242456 |
| A080419_03.log | 14:54:35 | 15:21:34 | 90.00 | 4855910 |
| A080419_04.log | 15:23:28 | 16:03:00 | 90.00 | 7112798 |
| A080419_05.log | 16:03:02 | 16:14:22 | 90.00 | 2034802 |
| A080419_06.log | 16:05:44 | 16:35:25 | 90.00 | 5339104 |
| A080419_07.log | 16:35:37 | 17:05:39 | 90.00 | 5402127 |
| A080419_08.log | 17:05:40 | 17:21:16 | 90.00 | 2800102 |
| A080419_09.log | 17:24:41 | 17:45:19 | 90.00 | 3706460 |
| A080419_10.log | 17:46:17 | 17:58:36 | 90.00 | 2208870 |
| A080419_11.log | 17:59:36 | 18:30:59 | 90.00 | 5642220 |
| A080419_12.log | 18:31:01 | 18:55:50 | 90.00 | 4459755 |
| A080419_13.log | 18:56:50 | 19:23:32 | 90.00 | 4801889 |
| A080420_00.log | 11:35:44 | 11:42:10 | 90.00 | 1152454 |
| A080420_01.log | 11:44:09 | 11:56:25 | 90.00 | 2202868 |
| A080420_02.log | 12:00:37 | 12:12:31 | 18.00 | 2136858 |
| A080420_03.log | 12:15:03 | 12:46:23 | 90.00 | 5636219 |
| A080420_04.log | 12:46:24 | 13:13:43 | 90.00 | 4906931 |
| A080420_05.log | 13:13:45 | 13:29:32 | 90.00 | 2839118 |
| A080420_06.log | 13:29:33 | 14:00:05 | 90.00 | 5492161 |
| A080420_07.log | 14:00:07 | 14:30:14 | 90.00 | 5414130 |
| A080420_08.log | 14:30:26 | 14:51:40 | 90.00 | 3817502 |
| A080421_00.log | 11:16:29 | 12:02:24 | 90.00 | 8262252 |
| A080421_01.log | 12:02:29 | 12:27:01 | 90.00 | 4408735 |
| A080421_02.log | 12:54:30 | 13:56:27 | 90.00 | 11149385 |
| A080421_03.log | 15:33:41 | 16:01:27 | 90.00 | 4993966 |
| A080421_04.log | 16:01:28 | 16:15:40 | 90.00 | 2551004 |
| A080421_05.log | 16:15:42 | 16:33:22 | 90.00 | 3175249 |
| A080421_06.log | 16:33:25 | 16:52:52 | 90.00 | 3499377 |
| A080421_07.log | 16:52:54 | 17:14:23 | 90.00 | 3862520 |
| A080421_08.log | 17:14:25 | 17:21:40 | 90.00 | 1299511 |
| A080421_09.log | 17:22:15 | 17:22:44 | 90.00 | 81032 |
| A080421_10.log | 17:23:24 | 17:35:29 | 90.00 | 2169854 |
| A080421_11.log | 17:35:32 | 17:49:16 | 90.00 | 2469972 |
| A080421_12.log | 17:49:18 | 18:11:48 | 90.00 | 4042590 |
| A080421_13.log | 18:12:30 | 18:29:50 | 90.00 | 3115226 |
| A080421_14.log | 18:29:54 | 18:43:23 | 90.00 | 2421953 |
| A080421_15.log | 18:43:27 | 18:59:16 | 90.00 | 2839118 |
| A080421_16.log | 18:59:17 | 19:14:26 | 90.00 | 2722071 |
| A080421_17.log | 19:14:27 | 19:29:35 | 90.00 | 2719070 |
| A080424_00.log | 11:35:59 | 11:50:12 | 90.00 | 2554005 |
| A080424_01.log | 11:50:14 | 12:05:36 | 90.00 | 2761087 |
| A080424_02.log | 12:05:39 | 12:20:08 | 90.00 | 2602024 |
| A080424_03.log | 12:20:10 | 12:33:23 | 90.00 | 2373934 |
| A080424_04.log | 12:35:10 | 12:50:58 | 90.00 | 2839117 |
| A080424_05.log | 12:51:03 | 12:59:06 | 90.00 | 1443569 |
| A080424_06.log | 12:59:07 | 13:03:10 | 90.00 | 723285 |
| A080424_07.log | 13:04:14 | 13:09:31 | 90.00 | 945372 |
| A080424_08.log | 13:10:53 | 13:14:08 | 90.00 | 579228 |
| A080424_09.log | 13:15:48 | 13:19:38 | 90.00 | 684270 |
| A080424_10.log | 13:21:03 | 13:21:42 | 90.00 | 111044 |
| A080424_11.log | 13:23:18 | 13:33:19 | 90.00 | 1797716 |
| A080424_12.log | 13:33:20 | 13:44:42 | 90.00 | 2040803 |
| A080424_13.log | 13:44:43 | 13:55:07 | 90.00 | 1866735 |
| A080424_14.log | 13:55:09 | 14:05:21 | 90.00 | 1830721 |
| A080424_15.log | 14:05:23 | 14:15:32 | 90.00 | 1821717 |
| A080424_16.log | 14:15:39 | 14:16:57 | 90.00 | 225090 |
| A080424_17.log | 15:55:48 | 15:56:01 | 90.00 | 33014 |
| A080424_18.log | 16:53:28 | 16:53:39 | 90.00 | 27011 |
| A080424_19.log | 16:55:14 | 17:05:10 | 90.00 | 1779702 |
| A080424_20.log | 17:05:11 | 17:16:22 | 90.00 | 2004789 |
| A080424_21.log | 17:16:23 | 17:25:44 | 90.00 | 1674659 |
| A080424_22.log | 17:25:45 | 17:35:20 | 90.00 | 1716675 |
| A080424_23.log | 17:35:21 | 17:37:49 | 90.00 | 438173 |
| A080424_24.log | 18:08:09 | 18:18:31 | 90.00 | 1857731 |
| A080424_25.log | 18:18:32 | 18:28:31 | 90.00 | 1788704 |
| A080424_26.log | 18:28:33 | 18:38:56 | 90.00 | 1860732 |
| A080424_27.log | 18:38:57 | 18:47:17 | 90.00 | 1494589 |
| A080427_00.log | 10:21:42 | 10:21:54 | 90.00 | 27011 |
| A080427_01.log | 10:26:30 | 10:35:58 | 90.00 | 1698670 |
| A080427_02.log | 10:35:59 | 10:45:49 | 90.00 | 1761695 |
| A080427_03.log | 10:45:50 | 10:59:38 | 90.00 | 2475976 |
| A080427_04.log | 10:59:39 | 11:11:09 | 90.00 | 2064814 |
| A080427_05.log | 11:11:10 | 11:16:01 | 90.00 | 864341 |
| A080427_06.log | 11:20:47 | 11:30:22 | 90.00 | 1716676 |
| A080427_07.log | 11:30:24 | 11:40:19 | 90.00 | 1779701 |
| A080427_08.log | 11:40:19 | 11:51:23 | 90.00 | 1983782 |
| A080427_09.log | 11:51:25 | 12:00:56 | 90.00 | 1707673 |
| A080427_10.log | 12:00:57 | 12:10:21 | 90.00 | 1686664 |
| A080427_11.log | 12:10:21 | 12:20:51 | 90.00 | 1878740 |
| A080427_12.log | 12:20:51 | 12:31:10 | 90.00 | 1848728 |
| A080427_13.log | 12:31:10 | 12:42:12 | 90.00 | 1977779 |
| A080427_14.log | 12:42:13 | 13:00:09 | 90.00 | 3220268 |
| A080427_15.log | 13:00:09 | 13:08:44 | 90.00 | 1536605 |
| A080427_16.log | 13:13:30 | 13:25:36 | 90.00 | 2172855 |
| A080427_17.log | 13:25:37 | 13:35:09 | 90.00 | 1713675 |
| A080427_18.log | 13:35:11 | 13:46:27 | 90.00 | 2022796 |
| A080427_19.log | 13:46:29 | 13:58:33 | 90.00 | 2163852 |
| A080427_20.log | 13:58:33 | 14:10:24 | 90.00 | 2127837 |
| A080427_21.log | 14:10:26 | 14:25:20 | 90.00 | 2680055 |
| A080427_22.log | 14:25:21 | 14:34:53 | 90.00 | 1707672 |
| A080427_23.log | 14:34:54 | 14:45:03 | 90.00 | 1821717 |
| A080427_24.log | 14:45:05 | 14:55:53 | 90.00 | 1938763 |
| A080427_25.log | 14:55:58 | 14:58:29 | 90.00 | 447176 |
| A080427_26.log | 14:58:52 | 15:03:34 | 90.00 | 840331 |
| A080427_27.log | 15:05:27 | 15:07:57 | 90.00 | 444175 |
| A080427_28.log | 15:08:42 | 15:10:52 | 90.00 | 384152 |
| A080427_29.log | 15:11:34 | 15:15:01 | 90.00 | 615243 |
| A080427_30.log | 15:16:09 | 15:18:19 | 90.00 | 384151 |
| A080428_00.log | 16:25:27 | 16:27:02 | 90.00 | 276110 |
| A080428_01.log | 16:38:10 | 16:51:57 | 90.00 | 2472974 |
| A080428_02.log | 16:51:57 | 17:00:18 | 90.00 | 1491588 |
| A080428_03.log | 17:00:19 | 17:10:11 | 90.00 | 1767697 |
| A080428_04.log | 17:10:11 | 17:20:37 | 90.00 | 1872737 |
| A080428_05.log | 17:20:39 | 17:31:21 | 90.00 | 1914754 |
| A080428_06.log | 17:31:21 | 17:40:14 | 90.00 | 1593628 |
| A080428_07.log | 17:40:15 | 17:51:08 | 90.00 | 1953769 |
| A080428_08.log | 17:51:09 | 18:00:08 | 90.00 | 1605632 |
| A080428_09.log | 18:00:09 | 18:10:22 | 90.00 | 1833722 |
| A080428_10.log | 18:10:23 | 18:20:06 | 90.00 | 1743686 |
| A080428_11.log | 18:20:07 | 18:26:56 | 90.00 | 1218480 |
| A080429_00.log | 14:38:26 | 14:49:22 | 90.00 | 1962774 |
| A080429_01.log | 14:49:24 | 14:59:26 | 90.00 | 1800709 |
| A080429_02.log | 14:59:40 | 15:09:19 | 90.00 | 1731682 |
| A080429_03.log | 15:09:21 | 15:20:01 | 90.00 | 1914754 |
| A080429_04.log | 15:20:03 | 15:30:16 | 90.00 | 1833722 |
| A080429_05.log | 15:30:17 | 15:40:15 | 90.00 | 1788704 |
| A080429_06.log | 15:40:16 | 15:44:49 | 90.00 | 810319 |
| A080429_07.log | 15:51:42 | 15:54:11 | 90.00 | 441175 |
| A080429_08.log | 16:00:36 | 16:02:45 | 90.00 | 378149 |
| A080429_09.log | 16:08:06 | 16:11:07 | 90.00 | 537212 |
| A080429_10.log | 16:16:36 | 16:26:48 | 90.00 | 1827719 |
| A080429_11.log | 16:26:49 | 16:36:38 | 90.00 | 1761694 |
| A080429_12.log | 16:36:39 | 16:46:25 | 90.00 | 1752690 |
| A080429_13.log | 16:46:26 | 16:56:16 | 90.00 | 1761694 |
| A080429_14.log | 16:56:17 | 17:08:45 | 90.00 | 2238881 |
| A080429_15.log | 17:14:09 | 17:25:28 | 90.00 | 2028798 |
| A080429_16.log | 17:25:29 | 17:35:13 | 90.00 | 1746688 |
| A080429_17.log | 17:35:15 | 17:43:58 | 90.00 | 1563616 |
| A080429_18.log | 17:45:28 | 17:59:23 | 90.00 | 2499984 |
| A080429_19.log | 18:00:50 | 18:10:18 | 90.00 | 1698669 |
| A080429_20.log | 18:10:19 | 18:20:08 | 90.00 | 1761693 |
| A080429_21.log | 18:20:09 | 18:33:07 | 90.00 | 2328917 |
| A080429_22.log | 18:33:08 | 18:41:26 | 90.00 | 1488586 |
| A080429_23.log | 18:41:27 | 18:52:45 | 90.00 | 2028799 |
| A080429_24.log | 18:52:46 | 18:59:52 | 90.00 | 1272501 |
| A080429_25.log | 18:59:56 | 19:06:06 | 90.00 | 1104435 |
| A080501_00.log | 13:51:54 | 14:02:07 | 90.00 | 1773699 |
| A080501_01.log | 14:02:09 | 14:12:07 | 90.00 | 1791706 |
| A080501_02.log | 14:12:08 | 14:22:19 | 90.00 | 1827720 |
| A080501_03.log | 14:22:32 | 14:33:37 | 90.00 | 1989784 |
| A080501_04.log | 14:33:39 | 14:45:15 | 90.00 | 2085822 |
| A080501_05.log | 14:45:17 | 14:56:29 | 90.00 | 2010792 |
| A080501_06.log | 14:56:33 | 15:05:30 | 90.00 | 1605633 |
| A080501_07.log | 15:05:31 | 15:15:05 | 90.00 | 1716676 |
| A080501_08.log | 15:15:06 | 15:26:33 | 90.00 | 2055810 |
| A080501_09.log | 15:26:35 | 15:35:39 | 90.00 | 1626641 |
| A080501_10.log | 15:35:41 | 15:47:17 | 90.00 | 2082820 |
| A080501_11.log | 15:51:22 | 16:00:38 | 90.00 | 1662654 |
| A080501_12.log | 16:00:39 | 16:10:47 | 90.00 | 1818716 |
| A080501_13.log | 16:10:48 | 16:20:36 | 90.00 | 1758693 |
| A080501_14.log | 16:20:37 |  | 90.00 |  |
| A080501_15.log | 16:43:32 | 16:55:54 | 90.00 | 2220874 |
| A080501_16.log | 16:55:54 | 17:05:09 | 90.00 | 1656652 |
| A080501_17.log | 17:05:10 | 17:15:41 | 90.00 | 1887743 |
| A080501_18.log | 17:15:41 | 17:25:10 | 90.00 | 1698669 |
| A080501_19.log | 17:25:11 | 17:36:54 | 90.00 | 2103828 |
| A080501_20.log | 17:36:55 | 17:46:42 | 90.00 | 1755691 |
| A080501_21.log | 17:46:42 | 17:56:05 | 90.00 | 1680662 |
| A080501_22.log | 17:56:05 | 18:07:28 | 90.00 | 2040803 |
| A080501_23.log | 18:58:44 | 19:00:54 | 90.00 | 381150 |
| A080501_24.log | 19:05:49 | 19:11:16 | 90.00 | 975384 |
| A080501_25.log | 19:15:19 | 19:19:09 | 90.00 | 684270 |
| A080501_26.log | 19:23:00 | 19:27:04 | 90.00 | 726287 |
| A080501_27.log | 19:31:18 | 19:35:30 | 90.00 | 750295 |
| A080501_28.log | 19:39:11 | 19:43:12 | 90.00 | 714281 |
| A080501_29.log | 19:49:45 | 19:54:58 | 90.00 | 933368 |
| A080501_30.log | 19:58:30 | 20:01:45 | 90.00 | 579228 |
| A080501_31.log | 20:06:40 | 20:11:34 | 90.00 | 876345 |
| A080501_32.log | 20:14:23 | 20:18:11 | 90.00 | 678267 |
| A080501_33.log | 20:22:03 | 20:26:20 | 90.00 | 765302 |
| A080501_34.log | 20:29:25 | 20:32:41 | 90.00 | 582230 |
| A080502_00.log | 13:44:29 | 13:55:04 | 90.00 | 1833723 |
| A080502_01.log | 13:55:06 | 14:05:07 | 90.00 | 1800710 |
| A080502_02.log | 14:05:09 | 14:15:26 | 90.00 | 1845728 |
| A080502_03.log | 14:15:27 | 14:25:12 | 90.00 | 1749690 |
| A080502_04.log | 14:25:14 | 14:35:42 | 90.00 | 1878741 |
| A080502_05.log | 14:35:43 | 14:45:13 | 90.00 | 1704671 |
| A080502_06.log | 14:45:15 | 14:55:11 | 90.00 | 1782702 |
| A080502_07.log | 14:55:12 | 15:01:02 | 90.00 | 1044411 |
| A080502_08.log | 15:18:20 | 15:30:03 | 90.00 | 2106830 |
| A080502_09.log | 15:30:05 | 15:40:43 | 90.00 | 1908752 |
| A080502_10.log | 15:40:44 | 15:50:02 | 90.00 | 1668657 |
| A080502_11.log | 15:50:04 | 16:00:02 | 90.00 | 1788704 |
| A080502_12.log | 16:00:03 | 16:08:39 | 90.00 | 1542608 |
| A080502_13.log | 16:26:52 | 16:36:05 | 90.00 | 1653651 |
| A080502_14.log | 16:36:06 | 16:45:02 | 90.00 | 1602631 |
| A080502_15.log | 16:45:03 | 16:55:02 | 90.00 | 1791706 |
| A080502_16.log | 16:55:03 | 17:05:03 | 90.00 | 1794706 |
| A080502_17.log | 17:05:04 | 17:15:06 | 90.00 | 1800709 |
| A080502_18.log | 17:15:07 | 17:22:47 | 90.00 | 1374542 |
| A080502_19.log | 17:51:42 | 18:00:03 | 90.00 | 1497590 |
| A080502_20.log | 18:00:04 | 18:10:02 | 90.00 | 1788704 |
| A080502_21.log | 18:10:03 | 18:20:21 | 90.00 | 1848728 |
| A080502_22.log | 18:20:22 | 18:30:19 | 90.00 | 1785703 |
| A080502_23.log | 18:30:20 | 18:37:23 | 90.00 | 1263497 |
| A080502_24.log | 20:51:41 | 20:51:58 | 90.00 | 42017 |
| A080502_25.log | 20:57:56 | 21:00:58 | 90.00 | 540213 |
| A080502_26.log | 21:05:21 | 21:15:19 | 90.00 | 1788705 |
| A080502_27.log | 21:15:20 | 21:25:03 | 90.00 | 1743688 |
| A080502_28.log | 21:25:04 | 21:35:02 | 90.00 | 1788705 |
| A080502_29.log | 21:35:03 | 21:45:05 | 90.00 | 1800709 |
| A080502_30.log | 21:45:06 | 21:55:04 | 90.00 | 1788705 |
| A080502_31.log | 21:55:05 | 21:59:17 | 90.00 | 750296 |
| A080502_32.log | 22:02:35 | 22:12:02 | 90.00 | 1695668 |
| A080502_33.log | 22:12:03 | 22:22:02 | 90.00 | 1788704 |
| A080502_34.log | 22:22:03 | 22:27:02 | 90.00 | 891352 |
| A080502_35.log | 22:27:03 | 22:37:02 | 90.00 | 1791705 |
| A080502_36.log | 22:37:04 | 22:47:02 | 90.00 | 1788704 |
| A080502_37.log | 22:47:03 | 22:51:18 | 90.00 | 759300 |
| A080505_00.log | 13:34:44 | 13:38:28 | 90.00 | 663262 |
| A080505_01.log | 13:46:44 | 13:51:10 | 90.00 | 789311 |
| A080505_02.log | 13:55:08 | 13:59:33 | 90.00 | 789312 |
| A080505_03.log | 14:03:17 | 14:07:48 | 90.00 | 804317 |
| A080505_04.log | 14:12:41 | 14:17:12 | 90.00 | 807319 |
| A080505_05.log | 14:20:07 | 14:21:06 | 90.00 | 171068 |
| A080505_06.log | 14:23:08 | 14:24:02 | 90.00 | 153061 |
| A080505_07.log | 14:26:55 | 14:27:39 | 90.00 | 123050 |
| A080505_08.log | 14:30:30 | 14:32:12 | 90.00 | 300119 |
| A080505_09.log | 14:49:31 | 14:59:42 | 90.00 | 1827720 |
| A080505_10.log | 15:11:40 | 15:21:10 | 90.00 | 1701670 |
| A080505_11.log | 15:21:10 | 15:29:49 | 90.00 | 1551611 |
| A080506_00.log | 12:05:40 | 12:22:44 | 90.00 | 2872132 |
| A080506_01.log | 12:22:46 | 12:32:07 | 90.00 | 1680663 |
| A080506_02.log | 12:32:08 | 12:42:08 | 90.00 | 1794707 |
| A080506_03.log | 12:42:09 | 12:52:04 | 90.00 | 1779701 |
| A080506_04.log | 12:52:05 | 13:02:17 | 90.00 | 1830721 |
| A080506_05.log | 13:02:18 | 13:12:03 | 90.00 | 1749689 |
| A080506_06.log | 13:12:04 | 13:18:16 | 90.00 | 1110437 |
| A080506_07.log | 13:32:26 | 13:45:36 | 90.00 | 2364931 |
| A080506_08.log | 14:00:47 | 14:11:11 | 90.00 | 1866736 |
| A080506_09.log | 14:24:08 | 14:31:23 | 90.00 | 1299512 |
| A080506_10.log | 14:41:29 | 14:56:19 | 90.00 | 2665049 |
| A080506_11.log | 14:56:42 | 14:56:57 | 90.00 | 39015 |
| A080506_12.log | 14:58:36 | 14:59:26 | 90.00 | 144057 |
| A080506_13.log | 15:00:22 | 15:02:04 | 90.00 | 300119 |
| A080506_14.log | 15:03:06 | 15:14:27 | 90.00 | 2037802 |
| A080506_15.log | 15:23:30 | 15:31:32 | 90.00 | 1437566 |
| A080506_16.log | 15:31:33 | 15:41:04 | 90.00 | 1707672 |
| A080506_17.log | 15:41:05 | 15:47:26 | 90.00 | 1137448 |

## Processed ASIRAS profiles

Following plots show all processed ASIRAS profiles. Each profile plot consists of four parts.

- Header composed of daily profile number and the date and a sub-header with the filename.

- Geographical plot of the profile (diamond indicates the start of the profile)

- Rough indication of the height as determined by the OCOG retracker plotted versus time of day in seconds.

- Info box with date, start and stop times in hour, minute, seconds, and in square brackets seconds of the day, acquisition mode etc.

It should be emphasized that the surface height determined by the OCOG retracker is a rough estimate and not a true height.

# Text boxes

x

y

Figure 2. Sketch of instrument installation in the Air Greenland Twin Otter.

Reference point for antenna offset measurements

Figure 3. Photographs of the Twin Otter installation.

Helicopter