## Slide 1: Exploring Earth's magnetic field and its environment with CryoSat-2
Nils Olsen DTU Space Technical University of Denmark

## Slide 2: Exploring Earth's magnetic field and its environment with CryoSat-2
Nils Olsen DTU Space Technical University of Denmark

## Slide 3: Exploring Earth's magnetic field and its environment with CryoSat-2
Nils Olsen DTU Space Technical University of Denmark
Earth’s magnetic field
Why using CryoSat ?
How ?
Applications
Thanks to: Giuseppe Albini, Jerome Bouffard, Tommaso Parrinello and the Technical Team of CryoSat

## Slide 4: Most satellites – including CryoSat - carry magnetometer for navigational purposes as part of their AOCS (Attitude and Orbit Control System) The data of these AOCS magnetometers have scientific value but data calibration is essential Towards a true swarm of satellites …

## Slide 5: Sources of the Near-Earth Magnetic Field

## Slide 6: Sources of the Near-Earth Magnetic Field
Internal sources
  fluid outer core: 94% electrical currents created by motion of a conductor
  crust: 3% permanent magnetization of minerals
  (mantle: induced currents due to time varying B)
External sources
  current systems in ionosphere and magnetosphere: 3%, but highly time-variable! caused by solar particles, fields, and radiation

## Slide 8: Why using CryoSat for exploring Earth’s magnetic field?
No high-precision magnetic field data are available between in the gap between CHAMP and Swarm (Oct 2020 and Nov 2013)
CryoSat helps to fill this gap, for improved study of the dynamics of Earth’s core field

## Slide 9: Why using CryoSat for exploring Earth’s magnetic field?
Ionospheric and magnetospheric electric current systems are oriented wrt Sun
Single satellites only measure at one specific local time (slowly drifting in time)
Simultaneous magnetic data from many satellites allows to detangle time-space structure of external sources
CryoSat-2, 1 Aug 2018
CryoSat-2, 1 - 29 Aug 2018

## Slide 10: Local Time evolution of Swarm and CryoSat-2
Swarm A/C change in LT of 2.73 hrs/month all LT in 4.4 months
Swarm B change in LT of 2.61 hrs/month all LT in 4.6 months
CryoSat-2 change in LT of 1.50 hrs/month all LT in 8 months

## Slide 11
Swarm only …
Swarm + Cryosat + CSES
Sven Kardol, http://orbits.tudelft.nl/

## Slide 12: The “secret instruments” of CryoSat-2
3 Vector Fluxgate magnetometers (FGMs)
3 Star imagers (STRs)
Estimation of calibration parameters requires FGM sensor output E and STR quaternions q and model values Bmod of the magnetic field vector at satellite position and time
Available: 4-sec sampled CryoSat-2 magnetic data E spanning 9.5 years (Aug 2010 – Dec 2018)

## Slide 13: Vector Calibration of FGMs
E is uncalibrated output of the 3 magnetometer sensor axes, BFGM is calibrated magnetic field vector in FGM frame
Assumption: linear response of each FGM instrument: 3 offsets (biases), 3 scale values (sensitivities), 3 non-orthogonalities
Alignment: rotation from FGM to CRF (Common Reference Frame of Star tracker) using STR quaternions q
3 Euler angles for describing rotation matrix
Estimation of the 12 parameters (offsets, scale values, non-orthogonalities, Euler angles) by a robust Least-Squares minimization of DB = BCRF,obs – BCRF,model where BCRF,model is magnetic field vector as given by CHAOS-6 geomagnetic field model (describing contributions from core, crust + magnetosphere)

## Slide 14: Accounting for temperature, s/c disturbance, and non-linearities
12 “basic” calibration parameters, estimated separately for each of the 100 months (Aug 2010 – Dec 2018) x 12 = 1200 parameters
The 3 offsets b and 3 scale values S depend on sensor temperature TFGM Assumed to be constant for whole mission: 2 x 3 = 6 parameters
Magnetic disturbance vector of Magnetorquer currents IMTQ Assumed to be constant for whole mission: 3 x 3 tensor = 9 parameters
Magnetic disturbances due to solar array and battery current strengths ISA1, ISA2, IBatt Assumed to be constant for whole mission: 3 x 3 = 9 parameters
Non-linearities (“transverse effect” disturbance of fluxgate sensor x on sensor output y) B1 depends on E32, and B3 depends on E23 and E32 : 3 parameters
In total 1227 model parameters estimated by robust non-linear Least-Squares from 13.3 mio observations (= 3 x 4.4 mio data triplets)
Temporal regularisation (smoothing) of month-to-month variation of “basic” 12 parameters

## Slide 15: Magnetic field strength F = |B| August 2018
observed Fobs
model Fmod
CryoSat-2
Swarm A
430 km altitude
720 km altitude

## Slide 16: Magnetic field strength F = |B| August 2018
Swarm A
DF = Fobs – Fmod
CryoSat-2, uncalibrated
Polar ionospheric currents

## Slide 17: Magnetic field strength F = |B| August 2018
CryoSat-2, calibrated
Swarm A
DF = Fobs – Fmod
Polar ionospheric currents
weaker in CryoSat, due to higher altitude

## Slide 18: Magnetic field strength F = |B| August 2018
CryoSat-2, calibrated
Swarm A
DF = Fobs – Fmod
dayside
nightside
1.9 nT rms measurement error: < 0.5 nT
6 nT rms
1 min (15 values) moving average

## Slide 19: Application: Monitoring of Magnetospheric Ring-current activity
Independent observation of time-evolution of magnetospheric ring-current with magnetic data from 5 satellites …
… and comparison with Dst-index derived from ground magnetic data
50 nT
Dst
CSES
GRACE-FO
CryoSat-2
Swarm B
Swarm A

## Slide 20: Space-time structure of magnetospheric field
Joint spherical harmonic analysis using magnetic data from 5 satellites
q10 is main ring-current term
describes symmetric ring-current in equatorial plane
Terms describing asymmetric ring-current
Strong asymmetric ring current during storm expansion phase contributions from terms with m = 1, faster decay compared to main term

## Slide 21: Application: Core surface field secular acceleration
CHAOS-6 model of Earth’s magnetic field up to spherical harmonic degree n = 19

## Slide 22: Application: Core surface field secular acceleration
Only ground observatories
Swarm
CHAMP
CHAOS-6

## Slide 23: Application: Core surface field secular acceleration
SOLA: Local Inversion of CHAMP, Cryosat and Swarm data (Hammer & Finlay 2019)
Swarm
CHAMP
Cryosat
CHAOS-6

## Slide 24: The Icing on the Cake Magnetic field of oceanic M2 tide determined from Cryosat data
Br of M2 tidal field at 720 km (Cryosat) altitude
Model prediction (ocean tidal flow model + model of conductivity for mantle, lithosphere and seawater
Courtesy: Alexander Grayver, ETH Zürich

## Slide 25: Summary and Conclusion
CryoSat has set new standards of what is possible with navigational magnetometers: (until now) the satellite with best magnetic data quality
Data can be used for core field studies and for investigating ionospheric and magnetospheric current systems - Space-weather applications
Enormous potential for science and application
Calibrated Cryosat-2 magnetic data (Aug 2010 – Dec 2018) are available as daily files (similar to Swarm L1b data) at ftp://swarm-diss.eo.esa.int/%23CryoSat-2

## Slide 26: Terminology …
Calibration: From Vector Fluxgate Magnetometer (FGM) 3-sensor output E to magnetic field BFGM vector in FGM frame Estimation of the parameters describing FGM calibration and applying them to data in order to get BFGM in physical units (nT) in an orthogonalized instrument frame
Alignment: Rotation of BFGM from FGM frame to Star Imager (STR) frame and further to BNEC in NEC (North-East-Center) frame Estimation of rotation parameters (“Euler angles”) and applying them to BFGM using STR attitude data q in order to get magnetic field vector in NEC frame
Characterization: Accounting for influence from instrument and/or S/C e.g. magnetorquer effect on FGM data, temperature dependence of FGM calibration parameters Estimation of disturbance parameters and correction of BFGM Often done by co-estimation with calibration parameters

## Slide 27: Temporal Evolution of Calibration and Alignment Parameters
For FGM3
Month-to-month variation:
Offsets: ± 8 nT
Scale values: ± 300 ppm
non-orthononalities and Euler angles: ±0.02°(±72 arcsecs)

## Slide 28: Daily rms misfit: 5 – 10 nT
BN: North component
BE: East component
BC: Downward component
F: Magnetic intensity

## Slide 29
Counter-rotating orbits
Swarm A/C vs B: October 2021
Swarm A/C vs CryoSat
Swarm B vs CryoSat
Conjunctions Swarm / CryoSat-2 Test case for “All-Swarm-satellites-in-one-orbital-plane” of October 2021

## Slide 30: Conjunctions Swarm-B / CryoSat-2 on 11 Oct 2016
CHAOS-6_x9 core removed