## Slide 1: Advanced Modelling of Geospace (AMOG) Using Satellite Platform MagnetometerS
Nils Olsen1, Fabrice Cipriani2, Elisabetta Iorfida2, Per Lundahl Thomsen1, and Flemming Hansen1
1DTU Space, 2ESA/ESTEC

## Slide 2: Most satellites carry magnetometer for navigational purposes as part of their AOCS (Attitude and Orbit Control System) The data of these AOCS magnetometers have scientific value but data calibration is essential
Towards a true swarm of satellites … AMOG project funded by ESA GSTP program

## Slide 3: Overview: The various satellite data sets
Name | NORAD ID | years | altitude
CryoSat-2 | 36508 | 2010 - | ≈ 720 km
SMOS | 36036 | 2009 - | ≈ 760 km
Aeolus | 43600 | 2018 - 2023 | ≈ 320 km
EarthCARE | 59908 | 2024 - | ≈ 395 km
Proba-2 | 36037 | 2009 - | ≈ 720 km
AWS | 60543 | 2024 - | ≈ 600 km
GRACE-FO C | 43476 | 2018 - | ≈ 500 km
GRACE-FO D | 43477 | 2018 - | ≈ 500 km
Main challenges:
AOCS magnetometer only active in safe mode: no continuous data
Coarse magnetometer sampling rate: 10 sec or lower (1 sec is appreciated)
Data resolution, e.g. 1 mT (1 nT is appreciated)
Large magnetic disturbances from s/c and other instruments
Green: operational data processing and provision Yellow: Not considered further, due to large magnetic disturbances or insufficient input data

## Slide 4: Magnetic Data from CryoSat-2
Launched in April 2010 – and still in operation
720 – 730 km altitude, 92° orbital inclination
3 AOCS vector Fluxgate magnetometers (FGMs), 4 sec sampling
3 Star imagers (STRs)
House-Keeping (HK) data available: magnetorquer currents, magnetometer temperature, …

## Slide 5: CryoSat-2
The Flagship AOCS mission – pushing the border of AOCS magnetometer processing
Determination of magnetometer calibration parameters (offsets, sensitivities, non-orthogonalities, Euler angles) and disturbance fields (magnetorquer, battery and solar array currents) by comparing of observed Bobs with Bref from CHAOS geomagnetic field model
Operational processing since January 2025: automatically processed in monthly batches, typically on 5th of each month Daily CDF files in “Swarm-like” format distributed through Swarm data server ftp://swarm-diss.eo.esa.int/Multimission/CryoSat-2
4-sec data version 0305 based on estimated parameters using data Aug 2010 - Dec 2025
New: Change in onboard operation and telemetry allows to obtain 1 sec data since Sept 2025 Operational processing of 1 sec data (version 0402, will replace the 4 sec 0305 data)

## Slide 6: CryoSat-2 – the various disturbances

## Slide 7: CryoSat-2 81-daily running mean of daily rms wrt CHAOS model
thick curves: nightside data thin curves: dayside data
below 5 nT rms in BC and F

## Slide 8: Further Successful Examples: Magnetic Data from GRACE and GRACE-FO Satellite Duos
GRACE-A and GRACE-B follow each other with 220 km alongtrack distance
Between March 2002 and October 2017, 89° orbital inclination, 480 – 500 km altitude
GRACE-FO 1 and GRACE-FO 2 follow each other with 220 km alongtrack distance
Launched in May 2018, 89° orbital inclination, 480 – 500 km altitude
Magnetic data routinely calibrated by GFZ

## Slide 9: New calibration of GRACE-FO data
67 months ”historical data” (June 2018 to Dec 2023) kindly provided by GFZ
Model parameterisation: 885 parameters (67 x 12 + 81)
12 ”basic” parameters (3 offsets, scale values, non-orthogonalitiies, Euler angles) in monthly bins
81 ”common parameters” (magnetometer non-linearities and temperature dependence, disturbances due to magnetorquer, battery and solar array currents) assumed to be constant for the whole mission
Model regularisation: minimize month-to-month variation of the 12 basic parameters reduces ”effective” number of model parameters from 885 to 203
GFZ: all parameters estimated separately for every month (67 x 99 = 6633 model parameters)
Higher data sampling rate of 2 Hz GFZ: 1 Hz
Model determined from northbound and southbound data for better separation of offset and scale values GFZ: either northbound or southbound data, with extrapolation to the other half of orbit

## Slide 10: GRACE-FO 81-daily running mean of nighttime rms wrt CHAOS model
below 5 nT rms in BC and F

## Slide 11: Aeolus
August 2018 – July 2023
Magnetoresistive magnetometer (no fluxgate) 10 sec sampling rate
Huge magnetorquer disturbances up to 30.000 nT non-linear relation between IMTQ and BMTQ
Daily CDF files for May 2019 – June 2023

## Slide 12: Aeolus 81-daily running mean of daily rms wrt CHAOS model
15 nT rms in BN larger in BC, BE, F
thick curves: 06 LT thin curves: 18 LT

## Slide 13: Aeolus
Despite the larger rms (> 15 nT) compared to CryoSat-2 ( ≈5 nT):
clear geophysical signal, in particular at polar latitudes (FACs)

## Slide 14: Altitude – “Swarm and Friends”
Swarm A/C
Swarm B
MSS-1
CryoSat-2
GRACE-FO A/B
CSES
Aeolus

## Slide 15: Local Time Evolution – “Swarm and Friends”
Swarm A/C all LT in 4.4 months
Swarm B all LT in 4.6 months
MSS-1 all LT in 26.3 days
CryoSat-2 all LT in 8.0 months
GRACE-FO A/B all LT in 20.2 months
CSES fixed LT at 02/14
Aeolus fixed LT at 06/18

## Slide 16: Conclusions
Calibrated magnetometer data available for CryoSat-2, GRACE, GRACE-FO, Aeolus, GOCE Daily files of calibrated AOCS magnetometer data freely available at ftp://swarm-diss.eo.esa.int/Multimission/
Challenges with AOCS magnetometer data from recent ESA EOP satellites, e.g. SMOS, EarthCare
  No continuous data (magnetometer only operating in safe mode)
  Coarse sampling rate of 10 sec or longer
  Large magnetic disturbances
Future: CryoSat follow-on mission CRISTAL to be launched in 2028, design similar to CryoSat-2 Fluxgate AOCS magnetometer, but different from the one on CryoSat-2