## Slide 1: magnetometer – Star-imager Alignment: Apparent Euler angle variation due to magnetospheric contributions Nils Olsen1, Karl Magnus Laundal2, Chris Finlay1, Lars Tøffner-Clausen1 with help from the usual suspects 1DTU Space 2University in Bergen/Norway
The Problem: “Time-changing Euler angles”
Polar Field-Aligned Currents during “quiet” conditions and their low-latitude magnetic signature
Impact on Euler angles
Conclusions / Recommendations

## Slide 2: Alignment of VFM Magnetometer and STR Star Imager
VFM magnetometer measures magnetic vector BVFM in the VFM instrument frame
STR measures attitude in the STR instrument frame
Transforming B to Earth-fixed vector requires knowledge of the rotation VFM  STR where is the matrix describing the rotation of B from the VFM frame to the star tracker frame, and is the rotation matrix from the STR to the NEC coordinate frame

## Slide 3: The VFM  STR rotation matrix R3
R3 is determined in-flight by comparing the observed vector BVFM,obs with a model vector BVFM,mod that has been rotated from BNEC,mod  BVFM,mod
R3 is often co-estimated with a magnetic field model BNEC,mod

## Slide 4: Apparent time changes of Euler angles
36”

## Slide 5: The VFM  STR rotation matrix R3
R3 is determined in-flight by comparing the observed vector BVFM,obs with a model vector BVFM,mod that has been rotated from BNEC,mod  BVFM,mod
R3 is often co-estimated with a magnetic field model BNEC,mod
Any magnetic field contribution that is not properly described by the field model may contribute to erroneous determination of R3 (i.e. of the Euler angles)

## Slide 6: The Evolution of Simplification …
Olsen and Stolle, 2012

## Slide 7: Presentation at QWG Paris, Sep 2015 Error in roll angle a due to in-situ currents
[nA/m2]
Magnetic field signature observed by a polar-orbiting satellite around local midnight can be equally well explained by
VFM-STR misalignment of 20” in roll angle a
Magnetospheric field in MLT frame
In-situ electric current density
Large-scale in-situ currents of  1 nA/m2 cause apparent Euler-angle mismatch of 20”
(Lühr et al., GRL 2015)

## Slide 8
Now: Error angle mismatch due to magnetic field produced by distant Field-Aligned Currents (FACs)

## Slide 9: Necessary Conditions for Spherical Harmonic Analysis of B
Assumption: data are taken in current-free region (  B = 0 in whole sampling region)
No spherical harmonic potential expansion possible if   B  0 in some region
Poloidal-toroidal decomposition is always possible:

## Slide 10: Magnetic signature from polar FACs in non-polar regions
Vector data B
at non-polar latitudes (contribute to Euler angles)
Scalar data F
at polar latitudes (do not contribute to Euler angles)

## Slide 11: Polar FACs during ”quiet” conditions 2 May 2014, Kp = 0o – 1-
Cat-2 product SW_OPER_FACATMS_2F_20140502T000000_20140502T235959_0201.DBL

## Slide 12: Polar FACs during ”quiet” conditions 2 May 2014, Kp = 0o – 1-
Cat-2 product SW_OPER_FACATMS_2F_20140502T000000_20140502T235959_0201.DBL
Northern Hemisphere Southern Hemisphere

## Slide 13: Polar FACs during ”quiet” conditions 26 Nov – 13 Dec 2013, Swarm A
Northern Hemisphere Southern Hemisphere

## Slide 14: Polar FACs during ”quiet” conditions Nov 2013 – March 2016, Swarm A
Northern Hemisphere Southern Hemisphere
Mean values, from CAT-2 FAC
Standard deviation, from CAT-2 FAC

## Slide 15: Polar FACs during ”quiet” conditions Nov 2013 – March 2016, Swarm A
Northern Hemisphere Southern Hemisphere
Determined using poloidal-toroidal decomposition of SIFMplus vector residuals

## Slide 16: Polar FACs during ”quiet” conditions Nov 2013 – March 2016, Swarm A
Northern Hemisphere Southern Hemisphere
Mean values, from CAT-2 FAC

## Slide 17: Summary: Polar FACs
Field-aligned currents (FACs) are always present at polar latitudes (> 60o magnetic latitude)
They connect ionosphere and magnetosphere, along field-lines of Earth’s main field (mainly dipolar)
Amplitudes are very varying, up to several 1000 nA/m2 even during ”quiet” conditions (as used for geomagnetic field modeling and Euler angle estimation)
250 nA/m2 is a typical order of magnitude mean value which we use in following

## Slide 18: Low-latitude magnetic field contribution due to polar FACs
Construction of 3D current system J
  FACs at top of ionosphere
  … closing currents in ionosphere (110 km altitude)
  … current continuation along field lines …
  … and possibly closing currents in magnetosphere.
Determination of magnetic field vector B due to this 3D current system using poloidal-toroidal decomposition of J and B (Olsen and Engels, 1998)
This magnetic contribution is not considered in any existing field model…
… and may therefore have impact on determined Euler angles

## Slide 19: Test with synthetic data
Swarm Alpha time and positions from SIFMplus data selection
Synthetic values of Bcore + BFAC
Rotated NEC  VFM frame using CCDB Euler angles (static)
Estimation of field model + Euler angles (in bins of 10 days) similar to what has been done with real data for SIFMplus (but only Swarm Alpha data, and no gradient data)
Excellent Euler-angle recovery if B = Bcore (no BFAC) (< 0.5” difference to CCDB in all 10-day bins)

## Slide 20: Test with synthetic data
Correct order of magnitude (250 nA/m2 yields up to 60” peak-to-peak), similar MLT dependence as observed, although different phase.

## Slide 21: Other possible R1/2 FAC models
The used FAC model (based on SIFMplus residuals) reflect annual mean, i.e. North-South symmetry Current closure in magnetospheric equatorial plane
But there probably exist some FACs connecting Northern and Southern polar regions (North-South asymmetry)

## Slide 22: Two simplistic elementary current systems
Symmetric / asymmetric R-1/2 currents of about 250 nA/m2 (much weaker than measured instantaneous currents) can explain Euler angle variation

## Slide 23: Conclusions
Ionospheric/magnetospheric currents are responsible for apparent change of Euler angles No ”Mysterious misalignments”
Polar FACs current densities of 250 nA/m2 can explain the observed LT variations This current densities are much lower (factor 5 to 10) then observed FACs, and thus small variations or persistent structures in FACs will cause the observed apparent Euler angle variation
No indication for true time-changing Euler angles constant (static) values should be used for L1b processing

## Slide 24: Much smaller time-variation in 2-3-1 Euler order frame
The two representations describe exactly the same rotation!

## Slide 25: Euler Vector Representation
Direction of vector yields rotation axis Amplitude proportional to rotation around axis (some similarity to first 3 elements of quaternions)