## Slide 1: Exploring Earth from Space – Towards a true Swarm of Magnetic Satellites
Nils Olsen, Lars Tøffner-Clausen, Clemens Kloss, Chris Finlay
DTU Space – Technical University of Denmark / DK
Satellites for measuring Earth’s magnetic field
On magnetometer data calibration
Cryosat-2 magnetometer data
Some scientific applications
Fully calibrated Cryosat-2 magnetic data (Aug 2010 – Dec 2018) are freely available as daily files in CDF (similar to Swarm L1b data) at ftp://swarm-diss.eo.esa.int/%23CryoSat-2

## Slide 3: Most satellites carry magnetometer for navigational purposes The data of these platform magnetometers have scientific value but data calibration is essential Towards a true swarm of satellites …

## Slide 4
Swarm
CSES China Seismo-Electromagnetic Satellite / Zhangheng 1

## Slide 5
Swarm
CSES China Seismo-Electromagnetic Satellite / Zhangheng 1
Cryosat

## Slide 6
Swarm only …
Swarm + Cryosat + CSES
Sven Kardol, http://orbits.tudelft.nl/

## Slide 7
Local Time evolution Swarm A/C + B and Cryosat

## Slide 8: Cryosat-2
Launched in April 2010 – and still in operation
720 – 730 km altitude, 92 degree orbital inclination
3 platform vector Fluxgate magnetometers (FGMs)
3 Star imagers (STRs)

## Slide 9: Terminology …
Calibration: From Vector Fluxgate Magnetometer (FGM) 3-sensor output E to magnetic field BFGM vector in FGM frame Alignment: Rotation of BFGM from FGM frame to Star Imager frame (CRF) and further to BNEC in NEC (North-East-Center) frame
Estimation of calibration and alignment parameters requires FGM sensor output E and STR quaternions q and model values Bmod of the magnetic field vector at satellite position and time
Available: 4-sec sampled Cryosat data spanning 9.5 years (Aug 2010 – Dec 2018)
Alternative to this sequential approach: Co-estimation of calibration + alignment parameters together with geomagnetic field model, to remove need for a-priori model values. See talk by Clemens Kloss IUGG19-3603 on Friday 12 July

## Slide 10: Vector Calibration of FGMs
E is uncalibrated output of the 3 sensors, BFGM is calibrated magnetic field vector in FGM frame
Assumption: linear response of each FGM instrument: 3 offsets (biases), 3 scale values (sensitivities), 3 non-orthogonalities
Alignment: rotation from FGM to CRF (Common Reference Frame of Star tracker)
3 Euler angles for describing rotation matrix 12 parameters

## Slide 11: Vector Calibration of FGMs
Estimation of the 12 parameters (offsets, scale values, non-orthogonalities, Euler angles) of by a non-linear robust Least-Squares minimization of DB = BCRF - Bmodel CHAOS-6,CRF where Bmodel CHAOS-6 is magnetic field vector as given by CHAOS-6 model (describing contributions from core, crust + magnetosphere)
Can also be done by solving for the 12 parameters of the linear inverse problem (9 elements of , 3 elements of ) followed by a (unique) determination of offsets, scale values, non-orthogonalities and Euler angles by QL decomposition of

## Slide 12: Accounting for temperature, s/c disturbance, and non-linearities
12 “basic” calibration parameters, estimated separately for each of the 100 months 100 months (Aug 2010 – Dec 2018) x 12 = 1200 parameters
The 3 offsets b and 3 scale values S depend on sensor temperature TFGM Assumed to be constant for whole mission: 2 x 3 = 6 parameters
Magnetic disturbance vector of Magnetorquer currents IMTQ Assumed to be constant for whole mission: 3 x 3 tensor = 9 parameters
Magnetic disturbances due to solar array and battery current strengths ISA1, ISA2, IBatt Assumed to be constant for whole mission: 3 x 3 = 9 parameters
Non-linearities (“transverse effect” disturbance of fluxgate sensor x on sensor output y) B1 depends on E32, and B3 depends on E23 and E32 : 3 parameters
In total 1227 model parameters estimated by robust non-linear Least-Squares from 13.3 mio observations (= 3 x 4.4 mio data triplets)
Temporal regularisation (smoothing) of month-to-month variation of “basic” 12 parameters

## Slide 13: Fully calibrated and aligned B, January 2014

## Slide 14: Temporal Evolution of Calibration and Alignment Parameters
For FGM3
Month-to-month variation:
Offsets: ± 8 nT
Scale values: ± 300 ppm
non-orthononalities and Euler angles: ±0.02° (±72 arcsecs)

## Slide 15: Daily rms misfit: 5 – 10 nT

## Slide 16: Data residuals are dominated by uncorrelated noise
Averaging over successive samples is recommended 5 sample average: 4 secs → 20 sec sampling
15 sample average: 4 secs → 60 sec sampling

## Slide 17: Application: Monitoring of Magnetospheric Ring-current activity
Orbit-by-orbit determination of “Dst-equivalent” from BN
Similar to Swarm MMA_F, but only P10-term

## Slide 18: Core surface field secular acceleration
CHAOS-6-x9 to degree n = 19

## Slide 19: Core surface field accelerations in equatorial region
Only ground observatories
Swarm
CHAMP
CHAOS-6-x9

## Slide 20: Core surface field accelerations in equatorial region
SOLA: Local Inversion of CHAMP, Cryosat and Swarm data (Hammer & Finlay 2019)
Swarm
CHAMP
Cryosat
CHAOS-6-x9

## Slide 21: The Icing on the Cake Magnetic field of oceanic M2 tide determined from Cryosat data
Br of M2 tidal field at 720 km (Cryosat) altitude
Model prediction (ocean tidal flow model + model of conductivity for mantle, lithospheric and seawater
Courtesy: Alexander Grayver, ETH Zürich

## Slide 22: Summary and Conclusion
Almost every satellite carries magnetometers for navigational purposes Their data can be used for scientific purposes – after calibration
Quality of magnetometer data and s/c disturbances is very different from satellite to satellite
Data can be used for core field studies and for investigating ionospheric and magnetospheric current systems - Space-weather applications
Enormous potential for science and application
Calibrated Cryosat-2 magnetic data (Aug 2010 – Dec 2018) are available as daily files in CDF (similar to Swarm L1b data) at ftp://swarm-diss.eo.esa.int/%23CryoSat-2
Cryosat is not Swarm – be prepared for surprises !